## Slide 1: New Marketing Strategies
Produced for the CRC for Premium Quality Wool undergraduate program by;
Dr. Paul Swan, Paul G. Swan & Associates Pty. Ltd.
Notes: Over recent decades, the global textile fibre market has changed rapidly. Largely, these changes have been brought about by changes to consumer preferences, continuing rapid expansion of the world population, emergence of new consumer markets, and increasingly intense competition between the major apparel fibres. As supplier of an historically important textile fibre, the wool industry has been forced to change with the changing circumstances, and new marketing strategies may be required for survival of the wool industry in the new millennium.
This module discusses some aspects of this changing market environment and examines one example of a new marketing strategy recently implemented.
Produced for the CRC for Premium Quality Wool undergraduate program by Dr. Paul Swan, Paul G. Swan & Associates Pty. Ltd.

## Slide 2: Our market share is declining
Paul Swan
Source: IWS (1993)
0.0
1.0
2.0
3.0
4.0
5.0
6.0
7.0
8.0
1960
1980
2000
2020
2040
Year
Wools
share
of the
fibre
market
(%)
Actual
Linear projection.
Quadratic projection
Projected
Notes: Written by: Dr. Paul Swan, Paul G. Swan & Associates Pty. Ltd.
Source: IWS Market Intelligence, 1997
Wool’s share of the apparel fibre market is declining at a rate of around – 0.1% per annum. At the current rate of decline, wool will be 1% of the total global fibre market in the year 2020. This figure is similar to that of the cashmere market at present (projection based on data 1970 - 1995).
The underlying reason for this rapid decline is that the apparel fibre market has grown dramatically over the period 1970 – 1995, while consumption and supply of wool as a textile fibre have remained largely static. IWS data (IWS Market Intelligence, 1997) shows that over the period 1970-1995 consumption of cotton and synthetic fibres increased by an average of 256 tonnes and 512 tonnes per annum respectively over the period 1970 – 1995, whereas consumption of wool increased by an average of 7.5 tonnes per annum.
Given that future supply of wool fibre will continue to be limited by water and land availability in relation to the price of the raw material, it is highly unlikely that the trend shown will reverse. To achieve reversal of the trend shown, supply and consumption of raw wool would need to increase at a rate greater than the rate of expansion of the apparel fibre market.
It seems likely therefore that wool will become an increasingly rare natural fibre, in the experience of the 21st century consumer.

## Slide 3: We have been technically static
Paul Swan
Source: Seaman, S. (1998)
Wool
US cotton
Polyester
Notes: Written by: Dr. Paul Swan, Paul G. Swan & Associates Pty. Ltd.
Source: Seaman, S. (1998) Genes to Suit, NSW Department of Agriculture
In addition to losing market share at a rapid rate over recent decades, wool has remained for the most part technically static in a period where major competitors have changed dramatically. This figure shows one aspect of the technical stasis of the wool fibre in relation to its’ competitors – that of average fibre diameter. Clearly, cotton and polyester have become finer as the years have passed, whereas wool has remained relatively constant.
To a large extent, the general reduction in fibre diameter achieved by the cotton and synthetic fibre industries has been driven by technical innovation in both production and processing, and through changes in consumer preferences. Such changes have altered the technical capability of these fibres.
The wool industry must also respond through technical innovation in production and processing, although such responses to a changing technical environment are difficult due to the nature of the wool industry. The supply base in the wool industry is made up of many thousands of individual producers and their many millions of individual sheep, the supply chain is long and fragmented, and the fibre is generally produced under tough and extensive conditions.

## Slide 4: We are also expensive as an apparel fibre
Cotton:
-$0.10 pa
Poly.:
-$0.07 pa
Paul Swan
Source: IWS (1993)
Notes: Written by: Dr. Paul Swan, Paul G. Swan & Associates Pty. Ltd.
Source: IWS Market Intelligence, 1996.
In addition to being predominately technically static over recent decades, wool is an expensive fibre in comparison to its major competitors. This is best seen in the prices for clean raw cotton, polyester, and wool for the period 1970 - 1995.
The data shows that despite the historically low prices for wool received through the mid 1990’s, the ratio of the cost of wool to the cost of cotton or synthetics has been slowly increasing over the past 3 decades (the wool:cotton ratio has increased by around + 0.06 units per annum, while the wool:synthetic ratio has increased at a rate of around + 0.02 units per annum since 1970).
This reflects the fact that the price of clean cotton has statistically declined at an annual rate of around 10.5 cents per kilogram per annum, whilst the price of polyester decreased by around 7.3 cents per kilogram per annum. Although there is little evidence in the data that these rates of reduction are slowing, we must accept that this will occur, otherwise the prices for clean cotton and synthetic fibres will reach zero in the years 2014 and 2025 respectively!
It seems unlikely that changes in the price of oil will significantly alter this picture in the short term. During the 1970’s OPEC oil crisis, oil prices rose markedly and yet there was no significant change in the long term price for polyester. This suggests that the price of polyester is relatively independent of the price of its’ raw material. This is probably reflecting the fact that polyester production has benefited from economies of scale and technological advances that have seen the unit price decrease, acting to cushion the fibre price from changes in raw material prices.

## Slide 5: Consumers are changing, and seek…
comfort
convenience
light weight, smart casual
ease of care
value for money
Paul Swan
Notes: Written by: Dr. Paul Swan, Paul G. Swan & Associates Pty. Ltd.
Sources: World Bank; Menswear/Haggar Fridaywear Survey, Cotton Inc. (1995); J. Grant, “R. & D. Challenges and Opportunities”, IWS (1996).
In addition to the changes in the relative costs, market shares, and technical characteristics of wool, cotton, and synthetic fibres, consumers of apparel are changing.
Today’s consumer is older (World Bank), more casual (Menswear/Haggar Fridaywear Survey, Cotton Inc. 1995), selective and environmentally aware (J.Grant, “R.&D Challenges and Opportunities”, IWS, 1996), and more closely focussed on personal satisfaction (IWS Updates, 1997) than ever before. Consumers are more strongly influenced by economic conditions, job security, and lifestyle changes than at any stage in the past. As a consequence, their apparel preferences have changed, becoming increasingly focussed on comfortable, light-weight, easy-care clothing which represents obvious value for money.
For wool to survive as a relevant, modern textile fibre, it must successfully compete in this increasingly tough and technically challenging consumer environment, and must be perceived by consumers as delivering at least some of the fabric attributes listed above. And it must compete as a fibre increasingly expensive, and relatively coarse by comparison to its’ major competitors.
Perhaps the only saving grace is the fact that our market share is declining at such a rate – this fact, in combination with our relative expense and technical stasis, suggests that wool will increasingly need to be positioned as a value-adding, luxury-type fibre.

## Slide 6: Fabric weights are declining
200
250
300
350
400
450
84
86
88
90
92
94
96
Year
Fabric
weight
(g/sq m)
Worsted
Woollen
Paul Swan
Data for Italian processors, Source: IWS (1993)
Notes: Written by: Dr. Paul Swan, Paul G. Swan & Associates Pty. Ltd.
Source: IWS Market Intelligence, 1996.
The degree to which consumers are changing in their fabric preferences is reflected by the types of fabric produced by knitters and weavers in response to changing retail requirements.
There has been a significant downward reduction over recent years in fabric weight, for both worsted and woollen fabrics. However, as with downward trends for commodity prices, these downward trends cannot continue indefinitely, from a perspective of the mechanical and thermal properties of fabrics. Some aesthetic properties of fabrics, such as drape, and the wear properties, such as abrasion resistance, also deteriorate at low fabric weights.
With increasing spinning, weaving, and knitting speeds, it is increasingly important that yarns be strong and even along their length. This technical requirement will only intensify as new technologies are implemented in the fabric and garment manufacturing industries.
These trends for increasingly light, yet strong yarns is being seen in the raw wool market, with substantial premiums for finer diameter fibres, and changing trade perceptions of commercial limits for ‘sound’ wool – where once 33 N/ktex would have been considered technically sound, the commercial limit is now closer to 42 N/ktex. In addition, the trade is becoming more aware of the importance of the mid-point break.
It seems likely that as the trade continues to strive for processing efficiencies while producing the light-weight products consumers increasingly prefer, pressures of wool growers to supply long, low diameter, and strong fibres will intensify.

## Slide 7: Summary
Relative to our competitors, wool is…
increasingly rare
    market share decreasing rapidly
increasingly expensive
    price ratio likely to increase
inefficiently processed
    high conversion costs; fragmented chain
Paul Swan
Notes: Written by: Dr. Paul Swan, Paul G. Swan & Associates Pty. Ltd.
In summary, wool’s future is as an increasingly rare, expensive natural fibre. It seems likely that the unit cost of wool yarns and fabrics in comparison to cotton or synthetic yarns or fabrics will remain high, given the seemingly divergent costs of the raw fibre, the relatively high cost of conversion of raw wool to wool garments, and the fragmented nature of the wool processing pipeline.
Another factor acting to undermine the competitive position of wool is that the wool industry is unable to react as readily as their competitors to the‘just in time’ (JIT) philosophy. This is a result of inelastic wool fibre supply (as an agricultural product), a long and fragmented processing pipeline, and the relative lack of volume in the market for some types of wool, especially at the fine end of the market.
As a consequence of declining market share, technical stasis, and seemingly increasing relative costs in relation to our major competitors, the competitive position of wool is irreversibly changing. So, what is the competitive strategy for the wool fibre for the 21st Century?

## Slide 8: Compete as a generic, commodity fibre ?
“..because of the relative complexity and
hence higher cost structure of the wool
yarn conversion route, wool (unless
heavily diluted with cheaper fibres) can
only be marketed in the mid - to – upper price levels of the garment industry, if the wool producer is to maintain reasonable profitability”.
Paul Swan
Source: AWC Report on Wool Marketing (1973)
Notes: Written by: Dr. Paul Swan, Paul G. Swan & Associates Pty. Ltd.
Source: AWC (1973), “Marketing Australian Wool”, Dec 1973, Chapter 4, pp 46 - 49. Quoted in: Report of the Wool Industry Future Directions Task Force (1999), Vol. 2, p 88.
The question often arises, when discussing the ills of the wool industry, how should wool compete in future? Should we seek to cheapen wool products and attract a much wider range of consumers in order to broaden markets and intensify demand (“..put a wool sock on every foot in China..”)? Or should we perhaps continue to target our promotional efforts on relatively wealthy consumers? Should woolgrowers abandon The Woolmark Company’s generic promotional campaign based around the Woolmark?
Needless to say, a successful competitive strategy for wool as a 21st Century textile fibre will need to be based around consideration of the fact that wools’ market share will continue to irreversibly decline, and wool will remain expensive to purchase in relation to our major competitors if the majority of growers are to have a realistic chance of survival as fibre producers. In addition, we need to acknowledge that, in relation to cotton or synthetic fibres, the wool fibre will probably remain relatively coarse and technically static from a product innovation perspective.
In this context, it hardly seems likely that a generic approach to marketing of wool as a bulk commodity is the way of the future. Rather, wool will need to compete as a value-adding luxury-type fibre.
It is ironic to note that in the mid-1970’s, the Australian Wool Corporation (as quoted above) made a similar assessment of the future wool market.

## Slide 9: 4 major competitive strategies
Broad segments
  Cost leadership (lowest cost producer)
  Differentiation (sole supplier)
Small market segments
  Focus cost (lowest cost producer)
  Focus differentiation
(premium $, specific segment, difficult to copy)
Paul Swan
Source: Porter, M.E. (1985)
Notes: Written by: Dr. Paul Swan, Paul G. Swan & Associates Pty. Ltd.
Source: Porter, M.E. (1985), Competitive Advantage: Creating and Sustaining Superior Performance, The Free Press, New York
Consideration of product marketing theory can shed light on the needed competitive strategy for the wool fibre for the 21st Century. Listed on the slide are 4 broad competitive strategies relevant for particular market segments, whether broad (volume) market segments or small markets, based on the work of Porter (1985).
Two general strategies appear to be used successfully in each of these market segments; one based on competing as the lowest cost provider of a particular product or service, the other being to differentiate oneself as sole supplier status of a particular product or service. The latter allows for higher margins.
The Cost Leadership strategy is used by large retailers competing in volume markets for mass-produced products, such as Target, K-mart, Big W, and Franklins. Differentiation strategies can also be used successfully in broad market segments, if an organization is a sole supplier of a specific, difficult-to-copy product. But generally, small market segments and limited supply imply a Focus Differentiation strategy.
Given that wool is expensive and an increasingly minor player in the global fibre market, the small market or focus segment strategies are most relevant. An example of this approach is ‘Niche Marketing’ - for more information, see the module, “Value Adding and “Adding Value””.

## Slide 10: A new strategy for the new millennium…
Paul Swan
    based on Focus Differentiation
abandon generic promotion
identify specific market segments
develop new markets
    Low weight, high purchase price, frequent purchase, hard to copy
facilitate technical innovation
    specification, easy care…..
achieve high quality standards
facilitate communication
    vertical integration?
Notes: Written by: Dr. Paul Swan, Paul G. Swan & Associates Pty. Ltd.
Considering the Focus Differentiation strategy and the likely competitive position of wool as discussed in the first section of this module, suggestions for a new general strategy for marketing wool are listed on this slide. As recommended in the 1999 Wool Future Directions Taskforce report, generic promotion should be abandoned. As also recommended, the technical advantages of wool should be highlighted especially in contrast to their competitor fibres.
It is imperative that new market segments be pursued, given the relative cost of the wool fibre and the slow decline of our traditional formal outerwear markets. In particular, wool should seek to have a presence in frequent purchase, high unit price, low unit weight products such as upper-market business shirts. In this particular market segment, well-heeled executives can and do pay for quality, convenience, and differentiation.
It is likewise imperative that we technically innovate throughout the pipeline and create opportunities to foster technical innovation. Innovations create opportunities for new wool marketing niches. To this end, new innovations in fibre measurement, such as fibre curvature, should be utilised to their fullest through the pipeline, breaking down barriers between different sectors through improving communication and confidence.
For an increasingly rare, expensive fibre such as the wool fibre, Quality and communication of Quality through the pipeline is extremely important. Nobody wishes to buy high priced rubbish. Truth in labelling and precise specifications need to be beyond question.
To this end, we perhaps need to see closer strategic alliances between different industry sectors, in effect bringing about vertical integration without joint investment in machinery.

## Slide 11: Homestead Grazing Co. Ltd.
An example of value chain management, and a focus differentiation strategy at work.
Paul Swan
Notes: Written by: Dr. Paul Swan, Paul G. Swan & Associates Pty. Ltd.
The next section of this presentation illustrates a focus differentiation strategy at work.
Homestead Grazing Co. Ltd. is a small company which seeks to control quality from raw material to retailer, maintain shareholder equity throughout the pipeline, and market high quality, difficult-to-duplicate products to late stage processors and end users. For a small player operating in an increasingly competitive marketplace, Homestead Grazing must achieve differentiation from competitors in terms of products and services, and product qualities. To this end, Homestead Grazing has a specific corporate structure which assists achievement of the above.

## Slide 12: Homestead Grazing Co. Ltd.
Mission:
Homestead Grazing (HG) will become a preferred supplier of high quality apparel yarn, fabric, and garments to selected manufacturers, designers, and consumers in Australia and overseas. In so doing, HG will provide shareholders with the opportunity to achieve dividends and increased equity in the wool value chain.
Structure:
Vertically integrated wool supplier and processor. Investment in relationships, not processing infrastructure.
History:
Incorporated 14th Nov. 1997
Paul Swan
Notes: Written by: Dr. Paul Swan, Paul G. Swan & Associates Pty. Ltd.
Homestead Grazing was incorporated in 1997, and the shareholding of the Company includes:
Wool growers in 5 states of Australia,
Wool processors (Topmaking/Spinning/Weaving/Knitting),
Fashion Designers, and
Wool Textile Scientists (facilitating communication between sectors).
From the outset, the intention has been to create a company whose shareholders represent every link in the wool value chain, so as to retain shareholder equity in the wool products through to marketing. In this sense, Homestead Grazing represents a vertically integrated wool processor, with the exception from the norm being that investment has been in the relationships, rather than in processing equipment.
Homestead Grazing seeks to become the preferred supplier of high quality yarns, fabric and garments to a specific market niches. Shareholders are given the opportunity to achieve dividends and increase equity in the wool value chain.

## Slide 13: Homestead Grazing Co. Ltd.
Shareholding:
Represents every link in the value chain from genetics to consumers (including marketers, fashion designers, weaver/spinners, topmakers, exporters, wool buyers, Stud Merino breeders, commercial wool growers, investors). Wide geographic spread of woolgrower shareholders.
Nature of business:
Production and marketing of yarn, fabric, and garments. Quality control throughout value chain.
Paul Swan
Notes: Written by: Dr. Paul Swan, Paul G. Swan & Associates Pty. Ltd.
Shareholders in this enterprise represent all areas in the value chain from wool grower to fashion designer and garment manufacturer. The business principles are the production and marketing of unique/technically difficult yarns, fabric and garments whilst maintaining quality control throughout the value chain.
Merino wool growers from a 5 states are shareholders in the company, including around 21 Merino studs. This supply base facilitates the sourcing of specific wool types from shareholders, creates new opportunities for control of product quality, and for shareholder profit.

## Slide 14: Homestead Grazing Co. Ltd.
Target market segment:
High quality, technically difficult, pure wool products.
Niches:
Men and Ladies fine gauge knitwear, and fine worsteds.
Focus of Differentiation:
End product quality, performance, and reliability
Technically difficult products.
Specific greasy wool types (superior processing qualities).
Paul Swan
Notes: Written by: Dr. Paul Swan, Paul G. Swan & Associates Pty. Ltd.
Homestead’s marketing philosophy is to target specific niche markets with a high quality pure wool product, technically difficult to produce, and therefore difficult to copy. Lightweight products are targeted, as these allow for the greatest margin per unit raw material, and are most suited to the contemporary and future consumer.
A key element of this strategy is raw wool supply. Specific, naturally rare greasy wool types with superior processing qualities (commonly known as ‘Elite Wool’) are the focus of the Homestead Grazing Company. Through sourcing such raw material, opportunities are created for efficiencies to be made throughout the processing pipeline, and end-products of superior quality and unique attributes in comparison to conventional wool products are produced.

## Slide 15: Homestead Grazing Co. Ltd.
Paul Swan
Key product attributes
Performance leader in all product niches
    Sensual softness
    Non-pill knitwear
    Rich colour palette, including pastels and ecru
    Enhanced drape
    Crease resistance
So for spinning and topmaking...
    Minimal fibre breakage, maximum fibre control
Notes: Written by: Dr. Paul Swan, Paul G. Swan & Associates Pty. Ltd.
A very small player (initially) in a competitive marketplace, Homestead Grazing needs to achieve differentiation from its’ competitors in all product niches. By virtue of the raw fibre selection strategy, and the vertical structure of the company, Homestead seeks to be the performance leader in the key product attributes of importance to consumers in all market niches, as listed above. For knitwear, for example, freedom from pilling and a rich colour palette are important.
To achieve the desired product attributes above, yarns needs to be of a guaranteed high quality and freedom from contaminants. To this end, topmakers and spinners need to minimise fibre breakage and maximise fibre control, and the raw fibre supply must be of the highest quality and uniformity of type, with very low risk of contamination.

## Slide 16: Wool Quality Targets
Paul Swan
Excellence in processing potential...
Excellent fibre alignment (character)
Low fibre curvature relative to the diameter
Long fibre length relative to the diameter
Uniformity and softness
Low mid-break percentage (< 30)
Measurable quality...
Conventional specifications, plus curvature
Notes: Written by: Dr. Paul Swan, Paul G. Swan & Associates Pty. Ltd.
The wool quality targets that Homestead Grazing strives to achieve are determined from working back from the product they wish to produce. To maximise fibre control in spinning, long average fibre length in top is sought, with minimal short fibre content and maximum uniformity and strength of individual fibres.
These top attributes imply certain raw wool attributes, including excellent staple crimp definition (signifying excellence of fibre alignment), low fibre curvature (broad crimp waves) in relation to the average fibre diameter, long fibre length in relation to the average fibre diameter, and uniformly low mid-break percentage (ideally < 30%) for all batch components.
Great care is taken to ensure that the raw material purchased is the raw material needed. Wools are selected by using conventional pre-sale measurements, in addition to fibre curvature measurement, detailed consideration of the display sample, the crutch:shear interval and the pack type. Ideally, the wool is sourced from grower shareholders.

## Slide 17: Wool Supply
Paul Swan
In order to make HG grow and satisfy clients:
  Source from shareholders if possible
  Make growers aware of requirements
  Develop forward contracts
  Forward pricing based on specific orders
  Clip analysis, planning, prediction
Interaction with stud networks
Notes: Written by: Dr. Paul Swan, Paul G. Swan & Associates Pty. Ltd.
In order to maintain wool supply and for Homestead Grazing (HG) to grow and satisfy clients, HG sources wool from shareholders where possible.
Communication between HG and growers allows for the development of forward contracts for specific orders, and HG assists the grower with clip analysis, planning and prediction. Dr. Mark Dolling has received support from AWRAP for the latter initiative.
Such interaction is facilitated by the involvement of Merino Studs as shareholders – these generally have existing close client networks.

## Slide 18: Clip Preparation and Quality Assurance
Paul Swan
Establish required standard of Clip Preparation
  Owner & Classer training (RIST, HG)
  Classing to meet specific market niches
  Flock management implications
Quality Assurance schemes
  Development of HG’s own
  Interaction with existing broker
Notes: Written by: Dr. Paul Swan, Paul G. Swan & Associates Pty. Ltd.
The standard of clip preparation required by Homestead Grazing is somewhat higher than the minimum standards contained in the current Code of Practice for Australian Wool Classers.
Through Homestead Grazing, owners and classers are able to receive specific training enabling classing of their wool clip to meet specific market niches. An inseparable issue is that of flock management, since the efficiency and quality of the classing job depends to a large extent on the makeup of the mobs as they run into the shed for shearing.
Homestead Grazing does not act as a wool broker, despite such close grower interaction and the development of its’ own quality assurance scheme. Rather, growers are free to deal with their existing wool selling broker if they wish, or may choose to market their wool through a broker of Homestead Grazing’s recommendation.

## Slide 19: Homestead Grazing Co. Ltd.
Clientele for initial processing batch
Fine gauge knitwear (2/54, 2/60, 2/72)
  Albert Spangaro (Melbourne)
  A&B Knitwear (Melbourne)
  Elegant Knitting (Sydney)
Fine Worsted cloth (2/80, 2/72)
  Business shirting, suiting & trouser materials
Paul Swan
Notes: Written by: Dr. Paul Swan, Paul G. Swan & Associates Pty. Ltd.
As an example of how the system works, consider the initial processing batch.
A range of products were identified as outcomes from the first processing batch – these were intended for specific processor clients, or specific market niches. In summary, fine gauge knitwear using a range of fine knitwear counts, and lightweight worsted cloth was produced.
For both of these broad product types, it was imperative that yarns be strong and very even, in addition to being light. The specifications of the raw fibre were an important consideration in achieving this level of yarn quality.

## Slide 20: Homestead Grazing Co. Ltd.
Characteristics of the greasy wool
Net Weight: 2214 kgs
Schlum. Yield: 80.3 %
V.M. content: 0.4 %
Diameter: 18.1 um
Staple length: 89 mm
Staple strength: 48 N/ktex
Mid break %: 37 %
Curvature 96o/mm
Paul Swan
Notes: Written by: Dr. Paul Swan, Paul G. Swan & Associates Pty. Ltd.
Listed on the slide are the specifications of the 2.2 tonnes net of wool used in the first HG processing batch.
As shown above, the raw wool was high yielding, long in relation to the average fibre diameter and very strong, with a low average mid-break level, and none of the component Sale Lots having greater that 50% mid-break content.
Fibre curvature was low for 18 m wool at 96 degrees/mm, being more like the fibre curvature seen in 19 - 21m wool.
Visual appraisal of the display samples ensured that each Sale Lot purchased was uniformly of good colour, free from Siromark, well classed and of excellent character and softness.

## Slide 21: Homestead Grazing Co. Ltd.
Actual H:
85.6 mm
TEAM H:
68.3 mm
% < 30 mm:
10.3 % less
mean: Team 2, histogram SiroHauteur ver 1.5c
Paul Swan
Notes: Written by: Dr. Paul Swan, Paul G. Swan & Associates Pty. Ltd.
As expected, the raw material processed efficiently to top stage and fibre breakage was minimised.
The graph shows the predicted fibre length distribution using the characteristics of the individual Sale Lots entered into the CSIRO’s SiroHauteur program (ver. 1.5c), in comparison to the actual fibre length distribution achieved at AusTops at Parkes in NSW..
The actual specifications of the top produced were a mean fibre length (Hauteur) of 85.6mm, with 3.7% of fibres less than 30mm. The top was very even (CV of Hauteur = 36%).
The predicted attributes were a TEAM Hauteur of 68.3 mm and using SiroHauteur, 10.3 % less than 30 mm, and a CV of Hauteur of 46%.
Thus, the top produced was far longer than normal commercial expectations would suggest, and far less fibre breakage and fibre wastage was experienced (6.1% noil). This result created the opportunity for HG to make savings on topmaking costs, while producing the sort of top able to be spun efficiently into the high quality yarns required.

## Slide 22: The Future??
Better communication through the pipeline
  virtual vertical integration
Defined technical niches (market segments)
  Hauteur : diameter, curvature, yarn weights
Paul Swan
Notes: Written by: Dr. Paul Swan, Paul G. Swan & Associates Pty. Ltd.
To conclude this module, I pose the question: “what does the future hold as a result of new marketing strategies? To answer my own question, I expect to see two particular changes in the wool industry, consistent with our future as an increasingly rare, expensive, value-adding, and luxurious natural fibre
Firstly, I believe the future will see better communication throughout the wool processing pipeline, leading to increased efficiency, technical innovation, quality control, and the opening of new market segments to the wool fibre. In large part, this will be achieved through more comprehensive understanding and specification of the technical attributes of the wool fibre, with key fibre specifications able to be traded throughout the pipeline. These specifications will allow a much more comprehensive understanding of key product attributes such as pilling, yarn evenness, next-to-skin comfort and handle and an ability for late-stage processors to translate this understanding into tradable fibre specifications.
With fibre-based communication between the different sectors of the processing pipeline, and the ability of late stage processors to specify the key fibre attributes underpinning product attributes of importance to consumers, our pipeline will become vertically integrated by default. This represents a major advance over our presently exporter/topmaker-dominated specification system.
A second major change, brought about by the above, will be increased grower and processor recognition of specific technical niches in relation to end-product types. As our understanding of wool processing and product attributes grows, it is becoming more and more apparent that certain combinations of fibre properties render wool fibres most suited to specific product. Like wine grape growers, wool growers will inevitably become more specialised and targeted toward specific market segments suiting their operations.

## Slide 23: Defined technical niches (market segments)
Top
Length:
Diameter
ratio
Yarn Weight
3
5
High twist, more
fibre ends
protruding,
fuller fabrics (e.g. suits)
Low twist factor,
high tenacity, sleek
soft fabrics, next
-to-skin (e.g. shirts)
Bulky knits,
Outerwear
Increasingly
Unconventional
H/D
Paul Swan
Notes: Written by: Dr. Paul Swan, Paul G. Swan & Associates Pty. Ltd.
This slide illustrates this concept, showing the different technical broad technical niches in relation to average fibre length in top (Hauteur) to diameter (H/D) ratio and yarn weight.
The ratio of Hauteur to diameter (mm/m) gives an idea of the relative fibre length of the top. For example, a top length of 80mm with a diameter of 20 m would yield a ratio of 4.
A H/D ratio for an average fine wool top would be 3 - 3.5:1. A top with a ratio of 4.5:1 is likely to be more even, stronger, and requires less yarn twist to achieve the same yarn strength. Such a yarn is suited to production of very lightweight weaving yarns, such as those produced by Homestead Grazing for the production of shirting material.
By comparison, formal suiting material usually requires heavier yarns with higher twist, generally producing a fuller fabric, often with raised fibre finish. For such products, an appropriate H/D ratio may be less than 4:1. For bulky knits, yarns are generally heavy and bulky. These generally have low H/D, as shown.
In the longer term, growers will be more attuned to the existence of these and other technical niches and will target their flocks and class their wool accordingly becoming more active participants in the wool processing pipeline.

## Slide 24: The Future??
Better communication through the pipeline
    virtual vertical integration
Defined technical niches (market segments)
    Hauteur : Diameter, curvature, yarn weights
Supply chain management
    HG, Wesfarmers, Fibre Direct….
Mature risk management system
Technically aware, market oriented growers
Paul Swan
Notes: Written by: Dr. Paul Swan, Paul G. Swan & Associates Pty. Ltd.
Besides what has been covered already in this module, in the future we will see more supply chain management organisations set up. Such organisations as Wesfarmers with Fibre Direct (see Fibre Direct module) are already established.
Price risk management schemes will reach maturation.
Wool growers will be more technically aware and market orientated, dividing their clips according to specifications in order to supply several different niches at same time.