## Slide 1: Dark Fibre Medullated Fibre
Produced for the CRC for Premium Quality Wool undergraduate program by;
Dr. Peter Auer, The University of New South Wales.
Notes: <number>
<footer>
This module examines the sources of isolated fibre contamination (medullation and dark fibre), the procedures available to ameliorate their effects, and the effect they have on final products such as fabrics.
Produced for the CRC for Premium Quality Wool undergraduate program by Dr. Peter Auer, The University of New South Wales.

## Slide 2: Dark Fibres
Peter Auer
Source: Foulds, R. A. et al. (1984)
Pigmented & Urine Stained
  Which is most common?
  What do they look like?
Notes: <number>
<footer>
Written by: Dr. Peter Auer, The University of New South Wales.
Source: Foulds, R. A., Wong, P. and Andrews, M. W. (1984), Dark Fibres and their Economic Importance, Wool Technology & Sheep Breeding, Vol. 32 (2), June/July.
Pigmented fibres are commonly thought to be responsible for the incidence of dark fibres in the wool industry. However work carried out by CSIRO Division of Wool Technology (DWT) (now Textile & Fibre Technology) indicates that a large number of dark fibres present in top samples from adult sheep are urine stained.
The difference between dark fibre and stained fibre is shown in this slide. Pigmented fibres are characterised by discrete pigment particles, while urine stained fibre is fairly evenly stained.

## Slide 3: Medullated Fibres
Wool Fibres with segmented medullation
coarse fibre
sparsely pigmented with
a continuous medulla
Peter Auer
Source: “Identification of Textile Materials” (1985)
Notes: Written by: Dr. Peter Auer, The University of New South Wales.
Source: “Identification of Textile Materials”, The Textile Institute, 7th Ed. 1985.
Fibres can be medullated in a number of ways as illustrated in this slide. Medullation can be complete or segmented.
The causes of medullation can be found at the follicle level; the result of differences within the follicle bulb. For more information see the relevant Wool Biology module.

## Slide 4: Detection
Medullation
  tops measured
  Projection Microscope
  OFDA
Dark Fibre
  tops measured
  Dark Fibre Detector (DFD)
Peter Auer
Source: Foulds, R. A. et al. (1984)
Dark Fibre
Notes: <number>
<footer>
Written by: Dr. Peter Auer, The University of New South Wales.
Source: Foulds, R. A., Wong, P. and Andrews, M. W. (1984), Dark Fibres and their Economic Importance, Wool Technology & Sheep Breeding, Vol. 32 (2), June/July.
Originally, the Wool Research Organisation of New Zealand (WRONZ) developed a machine to measure medullation. The South African Wool Technology Research Institute (SAWTRI) modified the design to produce their own instrument -- the medullameter. Measurement is based on the reflection of light. A test method entitled “Method of Test for Determining the Percentage of Medullated fibres by Projection Microscope” was first adopted by IWTO in 1964 (now IWTO-8-89). A later standard employs the image analysis capabilities of the OFDA apparatus (IWTO-57-96).
The photo in this slide illustrates how balanced light directed from below and above a spread fibre web can be used to make white fibre almost transparent and highlight any dark fibres. This is the basis for the CSIRO Dark Fibre Detector (DFD).
Detection of medullated and dark fibres is carried out on combed tops. Testing for dark fibre is not practical at the greasy stage (acceptable levels are about 4 staples per bale). Tests have been found to be most reliable at the top stage, since the wool has been sufficiently blended by then.

## Slide 5: Standards
IWTO-8-89
  Method for determining fibre diameter and percentage of medullated fibres in wool and other animal fibres by projection microscope
IWTO-57-96
  Determination of medullated fibre content of wool and mohair samples by opacity measurements using OFDA
IWTO(E)-13-88
  Counting of coloured fibres in Tops by the balanced illumination method
Peter Auer
Notes: Written by: Dr. Peter Auer, The University of New South Wales.
The Test Method for determining the percentage (%) of medullated fibres in a top sample is the standard IWTO-8-89 uses the Projection Microscope.
An ASTM standard, D2968 - 83, is also used to measure the percentage of medullated fibres.
The newer Optical Fibre Diameter Analyser (OFDA) is also capable of detecting medullated fibres, and is featured in the standard IWTO-57-96.
There is now a Test Method Under Examination (IWTO(E)-13-88) for the detection of coloured fibre in top. This method uses a Dark Fibre Detector (DFD).

## Slide 6: Control
Medullation
  breeding
  avoidance
Dark Fibre
  breeding
    pigmented not urine stained
  gene identification
    pigmented not urine stained
  avoidance
    pigmented and urine stained
Peter Auer
Notes: <number>
<footer>
Written by: Dr. Peter Auer, The University of New South Wales.
The incidence of medullation in a flock can be controlled by selective breeding based on fleece properties.
Similarly, dark fibre can be controlled by breeding, although genetic selection will only target pigmented fibres.
The has been some research done into the identification of genes which are responsible for pigment in fibres. For more information see the relevant Wool Biology module.
The avoidance of dark fibre which encompasses both pigmented and stained fibres is probably the most sensible method of controlling dark fibre for the woolbuyer.
The adoption of the Dark Fibre Risk Scheme would aid the woolbuyer in these endeavours.

## Slide 7: Dark Fibre Risk Scheme
Prediction
  probable risk to buyers
  CSIRO DWT development
Factors influencing dark fibre risk prediction
Breed
Age
Sex
Mulesed
Crutched
Crutch/Shear Interval
Shed Line
Risk
Peter Auer
Notes: <number>
<footer>
Written by: Dr. Peter Auer, The University of New South Wales.
The concept of the prediction method for dark fibre contamination was introduced as the Dark Fibre Risk Scheme in the late 1980’s.
The prediction scheme has the potential to highlight to prospective buyers the probable risk of contamination from pigmented or urine stained fibres in a particular sale lot.
Information on a properly completed woolclasser’s report can be used in the prediction of contamination levels for either pigmented or urine stained fibres. The information for breed, age, sex, mulesing, crutching, crutch/shearing interval and shed line in the form of a decision tree can be utilised to give a predicted risk of contamination.
The adoption of this technology has not been widespread to date.

## Slide 8: Effects of Final Products
Peter Auer
Medullation
  when dyed appear lighter in colour
  coarser kemp fibres tend to lie on surface of the yarn and fabric
Dark fibres
  smudge or dark line in white/pastel shades
  expensive to remove from fabric
Notes: <number>
<footer>
Written by: Dr. Peter Auer, The University of New South Wales.
Medullated fibres are not a problem until they are dyed. Internally reflected light makes the medullated fibres appear lighter, even though they absorb the same amount of dye into the protein.
Additionally, coarser fibres tend to migrate to the yarn surface during spinning and hence end up on the surface of the fabric. This is not desirable in terms of the surface finish of the fabric, although these fibres tend to be removed if they are raised from the surface. However, the lighter colour will be more apparent if these fibres are at the surface and bound in the fabric.
Makers of garments of white or pastel shades will not accept dark fibre contamination. The generally accepted level of contamination at the top stage is 100 dark fibres / kg (df/kg). This level is generally specified in a spinners specification to a topmaker. 100df/kg is equivalent of 4 staples or 1 g in an average bale of 165kg.
The fibres themselves will appear as a smudge or dark line in white or pastel dyed fabrics.
In both the cases of medullated and dark fibre, the individual fibres are very expensive to remove at the fabric stage. The product at this stage is also value added, so restoration is likely to occur, but claims for compensation will flow back to the spinner and then to the topmaker. Therefore, the expectations of risk of medullated and dark fibres will depress the price of suspect raw wool.

## Slide 9: Further Reading
Peter Auer
Foulds, R.A. (1988) “Dark fibre contamination in wool - Its prediction and ramifications”, The Technical Feasibility of the Sale of Wool by Description, Seminar Proc. (1988) CSIRO, Division of Wool Technology, pp127-139.
Notes: <number>
<footer>