## Slide 1: Colour Measurement Theory
Produced for the CRC for Premium Quality Wool undergraduate program by;
Andrew Lindsay, Australian Wool Testing Authority Ltd.
Notes: This module is designed to introduce the concepts behind the measurement of colour.
This work and the standardisation of colour measurement has been undertaken by an organisation called CIE (International Committee on Illumination), hence CIE Tristimulus Values, CIELAB etc. This organisation is still responsible for the standards associated with colour measurement, or colorimetry.
Produced for the CRC for Premium Quality Wool undergraduate program by Andrew Lindsay, Australian Wool Testing Authority Ltd.

## Slide 2: Colour Stimulus
Coloured Object
Observer
Light Source
Andrew Lindsay
Notes: Written by: Andrew Lindsay, Australian Wool Testing Authority Ltd.
There are three elements which when combined result in a colour stimulus (perception of colour) in the eye.
Light shines on a coloured object. The light can either be transmitted (i.e. the object is not opaque), absorbed by the object, or REFLECTED. In essence the measurement of colour is concerned with the measurement of this reflected light.
Therefore the perceived colour is affected by:
  the light source (e.g. objects appear a different colour at sunset since the composition of the light changes as the angle of the sun to the earth changes)
  the colour of the object, and
  the observer (e.g. some people are red/green colour blind, they lack the receptors in their eyes to see these colours.
Therefore to measure colour objectively we must use a STANDARD light source and a STANDARD observer.
The CIE Standard Observer refers to either a 2 degree or a 10 degree observation angle and was defined in 1931. This means that the angle of observation also affects colour perception.

## Slide 3: Visible Light
  Wavelengths
  absorbed
  transmitted
  reflected & become visible
Andrew Lindsay
Source: Colorimetric Fundamentals, datacolor international brochure
Notes: <number>
<footer>
Written by: Andrew Lindsay, Australian Wool Testing Authority Ltd.
Source: Colorimetric Fundamentals, datacolor international brochure, datacolor international, HQ Brandbachstrasse 10, CH-8305 Dietikon/Zurich, Tel: (41) 1-835 3800
The light that is associated with colour stimulus is defined as radiant energy of wavelengths from approximately 380 to 720nm. The diagram above demonstrates how light of various wavelengths is associated with different colours from Violet to Red.
The selective absorption of different amounts of the wavelengths within the violet - red spectrum determines the colour of objects. Different reflected wavelengths are associated with different perceived colours.
Those wavelengths not absorbed are those reflected or transmitted by objects, and thus visible to observers. For instance green objects absorb red and blue wavelengths. Yellow objects absorb blue wavelengths but reflect green, yellow and red wavelengths.
The colours are visible because that is how our eyes have evolved. Human eyes can’t perceive any wavelengths outside this spectral band. Some animals can see other wavelengths outside this band.

## Slide 4: Standard Illuminants
Andrew Lindsay
Source: Colorimetric Fundamentals, datacolor international brochure
Notes: Written by: Andrew Lindsay, Australian Wool Testing Authority Ltd.
Source: Colorimetric Fundamentals, datacolor international brochure, datacolor international, HQ Brandbachstrasse 10, CH-8305 Dietikon/Zurich, Tel: (41) 1-835 3800
The best light source would be the sun, which displays an even energy distribution across the visible spectrum. However the energy distribution of the sun is not easy to reproduce artificially. Therefore other light sources are used which approximate the sun.
The CIE has defined these the illuminants are::
A: Incandescent light (Tungsten)
B: Simulated noon sunlight
C: Simulated overcast-sky daylight
D: Simulated average daylight
One of the most common light source used to approximate daylight is called the Standard Illuminant D65. The slide shows the relative spectral energy curve for Daylight against A (a normal incandescent globe, Tungsten). As you can see D65 is relatively even across the visible spectrum, i.e. it approximates the white light of sunlight.
It can be seen that an object viewed under the Tungsten light source would be biased to the red end of the spectrum, and lack any blue input.

## Slide 5: Reflectance Curves
Andrew Lindsay
Source: Colorimetric Fundamentals, datacolor international brochure
Notes: Written by: Andrew Lindsay, Australian Wool Testing Authority Ltd.
Source: Colorimetric Fundamentals, datacolor international brochure, datacolor international, HQ Brandbachstrasse 10, CH-8305 Dietikon/Zurich, Tel: (41) 1-835 3800
This slide shows a number of Reflectance Curves for various colours.
Reflectance Curves are the most accurate way of representing the colour of an object. They are used by dyers and colourists to positively match colours.
Reflectance Curves are a measure of how much light is reflected by an object at each wavelength in the visible spectrum.
The reflectance for curves representing chromatic colours is highest in that part of the spectrum associated with that colour and drops to lower values at other wavelengths.
However, until recently the technology to cheaply reproduce Reflectance Curves was not available, so most industries use a system whereby perceived colour is converted into 3 values, representing the eye’s response to RED, GREEN and BLUE stimulation.
This system echoes the brain which doesn’t process the full spectrum but relies on receptors in the eye. These receptors respond to RED, GREEN and BLUE light according to the response of the Standard Observer.

## Slide 6: Tristimulus Values
Andrew Lindsay
Source: Colorimetric Fundamentals, datacolor international brochure
Notes: Written by: Andrew Lindsay, Australian Wool Testing Authority Ltd.
Source: Colorimetric Fundamentals, datacolor international brochure, datacolor international, HQ Brandbachstrasse 10, CH-8305 Dietikon/Zurich, Tel: (41) 1-835 3800
This slide shows how the CIE Tristimulus Values are derived.
The Spectral Energy function of the light source and Reflectance Curve of the object AND the SPECTRAL RESPONSE of the eye are combined mathematically to return the 3 values.
The Spectral Response curves for RED, GREEN and BLUE are shown at the bottom of the slide. These have been derived by averaging the response of a large population of people with normal colour vision, i.e. the CIE Standard Observer.
The usefulness of the Standard Observer is that it provides a standard means for converting any spectral curve into 3 numbers called CIE Tristimulus values, X, Y and Z.

## Slide 7: Colour Measurement
Three Tristimulus Values
  Red (X)
  Green (Y)
  Blue (Z)
Other systems related to this system
  L*, a*, b*
Y and Z are used for Raw Wool Colour measurement
Andrew Lindsay
Notes: <number>
<footer>
Written by: Andrew Lindsay, Australian Wool Testing Authority Ltd.
The outcome of colour measurement is the derivation of the Tristimulus Values which properly identify the colour of an object or light source in terms of the mixture of the primary lights (RED, GREEN and BLUE).
A problem with using X,Y,Z for colour matching is that they don’t provide uniform estimates of colour intervals or relationships. Other systems which provide more linear relationships between derived values have been derived such the L, a, b CIELAB system. Linear relationships are useful when colours are being specified.
However for the purpose of measuring the colour of wool, it has been determined by the industry that the use of X, Y, Z values is suitable. In particular Y is used to measure brightness or whiteness and Y-Z is used to measure yellowness.

## Slide 8: Wool Colour
Consider colour mixing:
Yellow + Blue (Z) = Green (Y) Yellow = Green (Y) - Blue (Z)
Y- Z is an indicator of yellowness
Y is an indicator of brightness
Andrew Lindsay
Notes: <number>
<footer>
Written by: Andrew Lindsay, Australian Wool Testing Authority Ltd.
Using the analogy of mixing paints, green is obtained by mixing yellow and blue. Therefore an estimate of yellowness can be obtained by subtracting blue from green.
Yellowness is the most important colour attribute for wool. It is estimated by subtracting the Z CIE Tristimulus value from the Y CIE Tristimulus value.
This formula is the one in use in the wool industry, even though more complex formulae for yellowness measurement exist. It has proved reliable over a fairly long period of time.
Brightness is of secondary importance and can be estimated by the Y CIE Tristimulus Value, which is the green component of the measured colour.
For more information on wool colour and the range of values found for wool colour in Australian Merino fleece wool see the module “The Measurement of Wool Colour”.