## Slide 1: Developments in Colour Measurement
Produced for the CRC for Premium Quality Wool undergraduate program by;
Mr. Andrew Lindsay, Australian Wool Testing Authority Ltd.
Notes: This module looks at some of the developments in the measurement of scoured wool colour that have occurred in the industry.
Produced for the CRC for Premium Quality Wool undergraduate program by Mr. Andrew Lindsay, Australian Wool Testing Authority Ltd.

## Slide 2: Measurement Developments
High between - instrument variability
  preparation
  instrument type & set-up
  cell design
Problems addressed
  cell design
  IWTO DTM 56
  WRONZ calibration wool
  AWTA tile standard trials
Andrew Lindsay
Notes: <number>
<footer>
Written by: Mr. Andrew Lindsay, Australian Wool Testing Authority Ltd.
During round trials between Australia and NZ, a high degree of between instrument variability was noted for the measurement of standard Interwoollab tops. This variability has been attributed to a number of factors:
the preparation techniques vary between the standards used in either country,
instrument types and and the way they are set up vary throughout the world, and,
cell designs differ between countries.
Proper cell design is covered in more detail on the following slide.
The differences between preparation techniques and instrument set-up will be addressed in the development of an IWTO standard test method which is at the draft stage.
A significant proportion of high between instrument variability was eliminated through the introduction of calibration wool by the Wool Research Organisation of New Zealand (WRONZ).
However, there are continuing shortcomings using a wool calibration standard. Because wool top standards can be soiled and are not durable, they are good for only a single use and can only be traced to that batch of wool used to make that standard. Therefore they are expensive and not traceable to an enduring standard.

## Slide 3: Wool cell design
Andrew Lindsay
Notes: <number>
<footer>
Written by: Mr. Andrew Lindsay, Australian Wool Testing Authority Ltd.
Wool to be measured is placed in the wool cell of the colorimeter. Wool cells are designed to present a flat uniform surface to the instrument.
There are a few design requirements:
- packing density 160 kg/m3
- infinitely thick layer of wool
- use of high quality optical glass
If these requirements are met the wool cells are quite functional and present no real problems in measurement.

## Slide 4: Imminent Developments
Andrew Lindsay
traceable calibration system
  standard tiles
Light source
  Illiminant C to D65
Observer
  2° to 10 ° observation angle
Notes: Written by: Mr. Andrew Lindsay, Australian Wool Testing Authority Ltd.
AWTA is investigating the use of certified tile calibration in wool colour measurement. This will overcome some of the shortcomings of using wool for calibration. A standard tile is certainly traceable, durable, can’t be soiled and ultimately less costly and more reliable.
The use of tile calibration standards is common throughout the colour measurement world.
The use of Illuminant D65 is now almost universal in colour measurement throughout the world. This simulates average daylight. Initially, the wool industry had adopted Illuminant C because of its ready availability. However, this and the observation angle will change with the adoption of Illuminant D65 and 10 degree observation angle into the IWTO standard.

## Slide 5: Effect of Scouring Changes on Y
60
61
62
63
64
1
5
9
13
17
21
25
Y
round trial period (weeks)
Andrew Lindsay
Notes: <number>
<footer>
Written by: Mr. Andrew Lindsay, Australian Wool Testing Authority Ltd.
The next two slides illustrate some research into colour measurement conducted at AWTA.
The same sheep running on different soil types were returning different colour values. The Yellowness results appeared too high for the sheep growing wool in the presence of red dust.
A student from the Department of Textile Technology at UNSW investigated this problem and found that the red dust was sticking to the wool with weak but significant van der Waals forces. This made the dust very difficult to remove in scouring.
A program of improved scouring including increased agitation, longer agitation, increased detergent levels, and uniform detergent delivery, increased water temperature, and a lot of trial work lead to an increase in brightness (this slide), and decrease in yellowness (next slide) for wool grown in red, dusty conditions.
It should be noted that these changes to scouring conditions have not been included in the new standard.

## Slide 6: Effect of Scouring Changes on (Y-Z)
round trial period (weeks)
1.4
1.6
1.8
2.0
2.2
2.4
1
5
9
13
17
21
25
Y-Z
Andrew Lindsay
Notes: <number>
<footer>
Written by: Mr. Andrew Lindsay, Australian Wool Testing Authority Ltd.
While this work is interesting, the fact is that processors face the same problem in removing red dust. Therefore the industrial results obtained for red, dusty wool would most likely be worse than for wool not containing dust of that sort.
In practice, processors will try and overcome this problem by blending this type of wool with wool of better colour quality to achieve a specified colour for their customer. They will still discount wool with red dust.