## Slide 1: Textile Processes & Products
Produced for the CRC for Premium Quality Wool undergraduate program by;
Dr. Peter Auer, The University of New South Wales.
Notes: This module describes textile processes in general, including those processes which are integral to the manufacture of blended fibre products.
An exercise is provided whereby textile products are matched to textile machines and processes. After this exercise, the complexity and inter-relations of the processing pipeline should be apparent.
Some textile processes not covered individually in this subject area such as weaving, knitting, dyeing and finishing are outlined in this module.
Produced for the CRC for Premium Quality Wool undergraduate program by Dr. Peter Auer, The University of New South Wales.

## Slide 2: Textile Products
Primary
  raw fibre
  continuous filaments
Secondary
  staple fibre
  scoured wool
  carbonised wool
  sliver
  slubbing
  top
  singles yarn
Final
  raw wool
  continuous filament
  scoured wool
  top
  singles yarn
  plied yarn
  fabric
    woven
    knitted
    felted (non-woven)
  garments
Peter Auer
Notes: Written by: Dr. Peter Auer, The University of New South Wales.
Primary textile products are fibres in the case of natural sources, and continuous filaments in the case of man-made and synthetis fibres.
Secondary products are grouped together here since they simply are products that form one step in the processing pipeline towards more processed products.
Final products are grouped here since they are tradable items. The textile pipeline is characterised by segmentation, so each of these products could be the final product of one member of the pipeline.

## Slide 3: Textile Processes
Early Stage (ESP)
  scouring
  carding
  gilling
  combing
  finisher gilling
Intermediate Stage (ISP)
  drawing
  spinning
  doubling
Later Stage (LSP)
  weaving
  knitting
  milling
  tufting (carpets)
  dyeing?
  finishing
  garment make-up
Synthetics
  tow cutting
  stretch breaking
Peter Auer
Notes: Written by: Dr. Peter Auer, The University of New South Wales.
The textile processes integral to the production of all the various wool products available today are categorised on this slide into ESP, ISP and LSP.
As you will see when the exercise is completed, the dyeing process, while usually thought of as LSP, may be undertaken at various points in the pipeline.
The processes of tow cutting and stretch breaking would be considered as intermediate processes in the production of synthetic staple yarn.

## Slide 4: Machines & Products: Exercise
INPUT
OUTPUT
Scour
Card
Gillbox
Comb
Finisher gillbox
Re-gilling
Re-combing
Drawing Frame
Spinning Frame
Doubling Frame
Loom
Knitting Machine
Milling Machine
Peter Auer
Notes: Written by: Dr. Peter Auer, The University of New South Wales.
This exercise details the input required and output received from each machine in the wool textile process.
The processes to match these machines would be:
Scouring
Carding
Gilling
Combing
Finishing
Drawing
Spinning
Doubling
Weaving
Knitting
Milling

## Slide 5: Processes & Products: Exercise
INPUT
OUTPUT
Tow Cutting
Stretch Breaking
Dyeing
Finishing
Garment Make-up
Peter Auer
Notes: Written by: Dr. Peter Auer, The University of New South Wales.
This table requires the name of the input and output product (or products) from the listed process. The shape and variety of machines used to undertake these processes is virtually endless and beyond the scope of this subject area.
However, a brief explanation of each process is included on the answer slide.

## Slide 6: Machines & Products
Scour
Card
Gillbox
Comb
Finisher
gillbox
Re-
gilling
Re-combing
Drawing Frame
Spinning Frame
Doubling Frame
Loom
Knitting Machine
Milling Machine
INPUT
raw wool
scoured wool
carbonised wool
other
fibres
sliver
sliver
combed sliver
wool top
other
fibre top
top
roving
slubbing
combed sliver (not wool)
singles yarn
plied yarn
singles yarn
plied yarn
raw wool
animal
fibre
yarn
OUTPUT
scoured wool
treated wool
wool sliver
slubbing
sliver
combed sliver
top
top
roving
singles yarn
folded yarn
plied yarn
woven fabric
knitted fabric
felted products
Peter Auer
Notes: Written by: Dr. Peter Auer, The University of New South Wales.
Items of interest in this table in the context of this subject area, i.e. wool technology to spinning, and blending, are highlighted in this slide.
Scour output can include treated wool. This category would include such things as insect-resist wool and flame -resist wool. In the latter two cases the same effect could be achieved during the finishing process. Shrink-proofing is usually applied after the top stage, since treatment at the fabric stage suffers in terms of aesthetics such as handle and drape, so this practice is not pursued in any great volume.
Scouring is also the first point where fibre blending occurs. Even though the fibre is chemically similar, the amount of variation inherent in a scour batch needs to evened out throughout the batch (up to 100 tonnes, usually about 50 tonnes).
The card is the next point where fibre blending is possible. This is certainly the case with woollen products (see “Processing on the Woollen System” module for more details). It is not a major point of blending for wool and other fibres in the worsted process due to the basic problem of fibre contamination, and also the specialised nature of wool early stage processors.
In the worsted process, usually the first point where wool fibre is blended with other fibres is during re-gilling and re-combing which preceeds the spinning process, and is either done by the spinners themselves, or by specialist blenders.
On the drawing frame, wool must be thinned down from a sliver to a roving before it can be spun on the spinning frame. (see “Drawing” module for more information). However, short staple fibres such as cotton and synthetics are able to be spun from combed sliver (tops), thus eliminating a process in the pipeline, but at the expense of some yarn properties. This process is called “open-end” (OE) spinning. This process has been tried unsuccessfully on long staple fibres like wool.
Until recently the singles yarn used in weaving would have been used exclusively in the weft direction (across the loom). A recent advance from WRONZ/CSIRO TFT has been the development of a singles yarn suitable for warp usage (see “Developments in Yarn Technology” module).
Singles yarn may also be used to produce a multi-component blend yarn with different fibres.
The Milling process uses the directional friction effect (DFE) inherent in animal fibre (wool, rabbit) to make felted products. The degree of felting may be controlled to give products such as blankets or hat felt.

## Slide 7: Processes & Products
INPUT
OUTPUT
Tow Cutting
continuous filament
staple fibre
Stretch Breaking
continuous filament
staple fibre
Dyeing
fibre
top
plied yarn
fabric
garment
dyed products
Finishing
yarn
fabric
finished products
Garment Make-up
finished fabric
sewing yarn
garments
Peter Auer
Notes: Written by: Dr. Peter Auer, The University of New South Wales.
Tow cutting and stretch breaking are two processes which achieve the same end by different means; both convert continuous filaments into staple fibres. Tow Cutting as the name suggests uses rotating blades to chop a “tow” of continuous filaments (up to a million filaments), while stretch breaking employs a twisting technique to cause the filaments to break into staple fibres. The subsequent fibre properties of converted fibres are different depending on the procees. This is especially true for the fibre length distribution.
Stretch breaking forms the basis of the technique used to manufacture “OptimTMfine” wool fibre, and “OptimTMmax” fibres, although in these cases the fibres are not stretched to breaking point. For more information see the “Modified Wool Fibre Technology (Optim fibres)” module.
Once the filaments are in staple form they are processed as staple fibres, usually into combed slivers (tops), which can then be made into pure or blended yarn. For more information see the “Blending Fibres” module.