## Slide 1: Style Instrumentation
Produced for the CRC for Premium Quality Wool undergraduate program by;
Dr. W. Humphries, CSIRO Textile & Fibre Technology.
Notes: <number>
<footer>
This module explains the instrumentation and metrology used to measure Style objectively.
The material is largely drawn from the CSIRO Division of Wool Technology’s seminar Woolspec 94. Copies of the proceedings are available from CSIRO Textile & Fibre Technology, formerly Division of Wool Technology.
Produced for the CRC for Premium Quality Wool undergraduate program by Dr. W. Humphries, CSIRO Textile & Fibre Technology.

## Slide 2: Prototype: Image Analysis
Colour + Shape Camera
Crimp Linescan Camera
Staples
Moving Belt
Printer
Computers
W. Humphries
Notes: Written by: Dr. W. Humphries, CSIRO Textile & Fibre Technology.
Computerised image analysis techniques form the basis of the objective measurement of greasy wool style. This development has been dependent on rapid, ongoing improvement in both computer and video technology, and it has resulted in more robust and less expensive technology which is suitable for use in a testhouse environment.
Basically, image analysis is a general term used to describe systems whereby an image is captured on a video camera. The digitised information is then transferred as an array of numbers to the memory of a computer where it is manipulated by mathematical functions (algorithms) in order to measure or highlight some feature of interest.
This diagram or schematic of one of the experimental prototypes developed by CSIRO shows the principles behind the measurement of the components of style. In the prototype, two separate image analysis systems were mounted over a belt which moved the staples past the cameras. One computer, camera and lighting system was dedicated to the measurement of the staple shape and staple colour attributes, while the other was for the measurement of crimp frequency and definition.
This experimental prototype was essential in determining the aspects critical to the objective measurement of style: for example, specific lighting requirements and algorithm improvements for the various style characteristics, and the design features required of the commercial prototype.

## Slide 3: Commercial Prototype
Camera
Lighting Frame
Tray Unloader
Staple Trays
Electronics Rack
W. Humphries
Notes: <number>
<footer>
Written by: Dr. W. Humphries, CSIRO Textile & Fibre Technology.
In the commercial prototype more consideration was given to staple handling and compatibility with testhouse computer systems. Therefore, it was decided to handle the staples in trays similar to those used with the ATLAS instruments for the measurement of staple length and strength. The computing power was transferred to a PC-based system.
The commercial prototype has an automatically controlled system not only to load and unload staple trays which are bar-coded for identification, but also to time the image capture sequences. Advances in cameras and computing have enabled a single camera to handle both the crimp and colour imaging, with optimised lighting providing the high-angle illumination for colour and shape analysis and low-angle illumination for the crimp analysis. This instrument is now being evaluated under testhouse conditions.
The throughput of the commercial instrument has been designed to be about 3 times that of the ATLAS length and strength tester. This ensures that the capital costs of implementing Style measurement can be minimised because the instrument can handle the throughput of 2 ATLAS machines.

## Slide 4: Image Analysis Measurements
Crimp Patterns
Size and Shape
Colour Profile
W. Humphries
Notes: <number>
<footer>
Written by: Dr. W. Humphries, CSIRO Textile & Fibre Technology.
Commercially it is envisaged that about 60 staples per sale lot would be measured prior to length and strength testing. The measurement of style using this instrument then involves a number of steps.
Three staple images are taken under different lighting conditions. The first lighting condition provides information on the colour of the staple, as well as its size and shape. The illuminant used enhances colour measurement. Once this image is digitised into red, green and blue (RGB) number arrays, it is relatively simple to tell the computer that very low numbers represent the black tray and high numbers are the staple area. Once the numbers that represent the staple are identified, this space can then be divided into 25 colour segments.
The difficulty has then been to determine which segment is wool and which is dust. This has been achieved with a second illuminant system using UV light. Wool fluoresces (looks blue) under this type of light, and therefore it is simple to tell the computer to differentiate the fibre segments from dust segments (which don’t fluoresce). Similarly, wool at the tip can be differentiated as weathered.
So, each colour segment can be designated as either dust or wool, then the greasy wool yellowness and dust colour can be measured objectively using the RGB number arrays.
The third image provides information on the crimp of the staple. The illuminant is angled to the staple so that the top of the crimp looks bright and the trough of the crimp appears dark. This spatial array of high and low numbers can be processed by the computer using a mathematical technique called Fourier Transformation into a frequency array. The peak of this frequency array is the primary / dominant crimp of the staple.
Another difficulty has been to decide how to define crimp definition. As crimp becomes less defined the differentiation of the frequency peak becomes less sharp. Therefore the crimp definition is related to the shape of this peak. A high narrow peak indicates a staple of good crimp definition.

## Slide 5: Inferred Staple Attributes
SIZE
SHAPE
COLOUR
PROFILE
CRIMP
Width, Length
Tip
Weathered Tip
Dust (Colour & Penetration)
Greasy Colour
Stain Bands
Crimp Frequency
Crimp Definition
Cottedness
W. Humphries
Notes: <number>
<footer>
Written by: Dr. W. Humphries, CSIRO Textile & Fibre Technology.
The heart of style metrology is in devising methods for extracting and interpreting style component information from the staple images, i.e. telling the computer what to do with the numbers.
This is done through the development of computer algorithms. These instructions derive the information from the digitised staple images, as well as make comparisons with a large database of staples of known attributes. Algorithm development is still evolving, and the final algorithms are subject to copyright.
This list on this slide shows the style attributes that are inferred from the shape, crimp and colour data. From the size and shape information we have width and length measurements and tip information, i.e. whether the tip is blocky, or more tippy, or like a lamb’s tip.
From the crimp data we extract the crimp frequency and also calculate the crimp definition, i.e. the clarity and uniformity of the crimp along and across the staple.
Finally the colour profile is interpreted. This is more difficult as it involves identifying the coloured zones, locating them and classifying them in terms of dust, wool and weathered wool. This has been made easier with the use of the UV illuminant system.

## Slide 6: Style Metrology Results
W. Humphries
between
Instrument
Variance
between
Replicate
Variance
R²
0.84
0.36
0.70
0.62
0.67
std
2.84
0.86
0.21
4.24
1.16
Length
Tip Length
Crimp Frequency
Crimp "Definition"
Brightness
Yellowness
R²
0.99
0.91
0.91
0.92
0.97
0.96
std
0.8
0.3
0.12
6.38
0.41
0.16
Notes: <number>
<footer>
Written by: Dr. W. Humphries, CSIRO Textile & Fibre Technology.
A preliminary between-instrument trial has been carried out to quantify between instrument and between sample replicate variances. Two instruments were involved each measuring two replicate samples of one hundred lots.
It can be seen from this slide that the agreement between instruments measuring the same samples is very good and would be acceptable for a commercial test. However, the agreement between measurements of replicate samples on the same instrument is not as good. In particular, there is a poor correlation between samples for tip length. This is thought to be a function of staple preparation.
These results are preliminary in nature but it appears that sampling may the largest source of variation in this test. It would be uneconomic to change the sampling procedures therefore, based on additional data, the industry will have to decide whether the precision which can be achieved by the instrument is sufficient for commercial trading.
However, it is very likely that the precision achieved by this objective measurement will be much better than that achieved by subjective appraisal of style attributes.
Currently three commercial instruments are being trialled. It is hoped that an interlaboratory round trial will be carried out in the near future to provide precision data for a draft standard.