## Slide 1: Customer Preferences (Topmaker & Spinner)
Produced for the CRC for Premium Quality Wool undergraduate program by;
Michael Blake, Chargeurs Wool Eurasia.
Notes: The ultimate demand for a product lies with the consumers of that product. Their preferences and ability to buy at any one time will influence the demand for that product. In the case of wool apparel products such things as season, fashion and economic security play an important role in customer demand.
This module addresses the demands placed on an Australian topmaker in today’s competitive environment.
Produced for the CRC for Premium Quality Wool undergraduate program by Michael Blake, Chargeurs Wool Eurasia.

## Slide 2: Chargeurs
largest wool processor in the world
  globalised, centralised European/Asian operation
  120 million kg top p.a. world-wide
Australian operations
  commercial / strategic
    Chargeurs Wool Eurasia
  buying (auction & direct to mill)
    Prouvost Hart
  processing to top stage
    Riverina Wool Combing (Wagga Wagga)
Michael Blake
Notes: Written by: Michael Blake, Chargeurs Wool Eurasia.
Chargeurs is an example of an international topmaking business with interests in Australia and overseas. It is the largest wool processor in the world with operations centralised in Europe and Asia. It produces approximately 120million kilogram of top per year and operate on a 24hour clock world-wide.
The Australian operations consist of Chargeurs Wool Eurasia, Prouvost Hart and Riverina Wool Combing (Wagga Wagga).
Chargeurs Wool Eurasia, the commercial strategic arm of Australian operations is where the decisions to buy or sell are made. Prouvost Hart, the buying organisation uses all avenues available to purchase wool, from auction to directly off farm. The early stage processor Riverina Wool Combing is the largest in Australia, processing 18% of the Australian clip.

## Slide 3: Raw Wool Demand
Consumer Demand
Fashion / clothing manufacturers
Weavers / Knitters
Worsted Spinners
Topmaker
Raw wool supply
Michael Blake
Notes: Written by: Michael Blake, Chargeurs Wool Eurasia.
The demand for raw wool ultimately lies with the consumers’ demand for certain apparel items. The consumer may be influenced by advertising, fashion, lifestyle and wealth. This demand is then passed down the processing chain to the various players (as seen in this slide).
The double arrow between the top-maker and the spinner, indicates that the spinners’ demand for a certain product is transmitted through the spinner’s specifications to the topmaker, while the ability of the topmaker meets that need by availing himself of the raw wool.

## Slide 4: Derived Demand (raw wool)
consumer needs and wants
fibre related
  weight
  drape
  handle/tactile
  surface appearance
processor requirements
service related
  reliable supply
  delivered on time
  giving repeatable performance
  helping high efficiency
Source: Stanton, J. (1998)
Notes: Written by: Michael Blake, Chargeurs Wool Eurasia.
Source: Stanton, J (1998) Derived Demand for Raw Wool, Wool Marketing, CRC undergraduate lecture.
The demand for the raw wool comes from both the consumer’s needs and wants and the processors requirements to meet those demands.
Consumer demand moves according to fashion and season. The fibre related factors that influence the decision of the consumer to purchase are weight of the fabric or garment, drape, feel and appearance.
The processor requirements are service related with the most important being reliable supply of a consistent raw product. The top-maker must supply 365 days a year, delivering on time, and with a product that is of a high quality and repeatable performance.

## Slide 5: Factors affecting Topmakers
cost of topmaking in Australia
seasonality of supply
demand from spinner
“least cost” solution to specifications
Michael Blake
Notes: Written by: Michael Blake, Chargeurs Wool Eurasia.
There are several interrelated factors that affect a topmaker’s operation.
Topmakers are constantly being affected by the cost of their operation. This is influenced by the seasonality of supply and the changing demands of the spinner, who, in turn, is influenced by changes in the market place.
The topmaker is constantly attempting to blend wools at “least cost” by juggling availablility of supply of certain types of raw wool to satisfy the specifications of the spinner. The spinners’ specifications do not take into account the seasonal changes in the supply of particular types of raw wool e.g. Superfine wool.
Some of these factors will be expanded on in the following slides.

## Slide 6: Cost of Topmaking in Australia
macroeconomic issues
  exchange rates
  interest rates
low margins (see next 2 slides)
high cost
  efficiency
  technology
  staff expertise
processing relocation
close to raw material source
Michael Blake
Notes: Written by: Michael Blake, Chargeurs Wool Eurasia.
The cost of topmaking in Australia depends on several factors. The broader picture of exchange rates and levels of interest rates will determine Australia’s position in the global financial market and hence the competitive cost of products manufactured in Australia.
The topmaker works on very low margins. This issue is covered in more detail in the next two slides.
The structure of the topmaking company, labour , logistics and financial issues, such as taxes and interest rates all contribute to the high costs incurred by the topmaker.
Cost reductions can be achieved by concentrating on production efficiency and technology advances. The efficiency of the topmaking facility can be achieved through increased size of the operation, as well as the use of measured raw wool. Technological advances such as the latest equipment and the expertise of staff play a role in the overall financial viability of the topmaking plant.
Globally, there has been a trend for topmaking to move to lower cost production units in either cheaper countries or sites.
However, a positive for the Australian based topmaker is their proximity to the raw material thus elimating some of the transport costs.

## Slide 7: Share of Final Costs: Wool
Michael Blake
Source: Stoeckel, A. et al. (1990)
Notes: Written by: Michael Blake, Chargeurs Wool Eurasia.
Source: Stoeckel, A., Borrel, B. and Quirke, D. (1990) Wool into the 21st Century, Implications for Marketing and Profitability, Centre for International Economics, Canberra.
This slide shows a breakdown of the costs incurred in the making of a man’s woollen suit. While this slide is from 1990, it does demonstrate the ratios of costs that are still found in the industry today.
As can be seen, a large part of the cost is found outside the first stage processing area. As far as early stage processing is concerned, the slide shows the low margins involved in top-making It also shows that a very large part of the the cost of a top is made up from raw material costs.

## Slide 8: Topmaking Costs
Michael Blake
Source: The Wool Task Force (1999)
$1.35 to $1.80 / kg
depends on
  diameter
  yield
  clip preparation
  scour location
contamination
  14c / kg
effluent
  20c / kg W. Europe
  5c / kg Australia
risk costs
  client complaints
  non-guarantee
  1.5c / kg
raw material
  70% of total
Notes: Written by: Michael Blake, Chargeurs Wool Eurasia.
Source: Wool Future Directions Taskforce (1999), Taskforce Report
The figures shown in this slide were taken from ‘The Wool Task Force Report, (1999)’ and are not those of any particular topmaking enterprise.
The costs that will be incurred by the topmaker are greatly influenced by the raw product. A dirty, low yielding wool will be far more expensive to process than a clean, high yielding wool. Wools of different diameters process differently; a finer wool being harder and more expensive to process than a coarser wool. A poorly prepared clip or a contaminated lot being part of a consignment may override all others and ultimately lead to lot rejection, or a claim against the topmaker. The proximity of the scouring plant to the topmaking facility will diminish transport costs.
The cost of effluent treatment in Australia is cheaper than that in Europe where very high-tech expensive solutions are employed. Australia is however more expensive than some third world countries where no effluent control is employed at all.
The non-guarantee from the grower of the quality of the raw wool means that the topmaker carries the risk of costs incurred through client complaints and lot rejection through contamination. The figure of 1.5c/kg would be for the physical product only.
The major cost to the topmaker is the purchase of the raw material. It accounts for 70% of total costs.

## Slide 9: Seasonality of Supply
wool availability throughout season
  supply - demand imbalance
  specific types at specific times
  fresh wool supply is falling
  competing against exports
  no imported raw wool
stock holding costs
  financial
  storage capacity
Michael Blake
Notes: Written by: Michael Blake, Chargeurs Wool Eurasia.
The lack of year-round availability of all types of wool creates an imbalance of supply and demand.
The spinners and weavers want a continuous supply of a reproducible and consistent product. To this end, the Australian topmaker competes against off shore topmaking facilities which can import wools from countries such as South America and South Africa and combine them with Australian wool to meet the required specification. Only raw wool from New Zealand may be imported into Australia. On a volume basis, NZ production is next to nothing. This is a disadvantage for Australian topmakers.
In order to cope with seasonality of supply, the Australian topmaker may buy above market value to secure stocks of wool that it may be unable to acquire later in the season. This stock is then held in storage so that the topmaker can continue to meet the spinners specifications. Both the extra purchase costs and the storage costs place an increased financial burden on the topmaker.

## Slide 10: Means of Raw Wool Supply
auction
private treaty
futures
  SFE
  Macquarie
stockpile forward sales
trade
sale by description
electronic selling
Michael Blake
Notes: Written by: Michael Blake, Chargeurs Wool Eurasia.
Any and all avenues are used to secure supply. The methods of procuring wool are listed on this slide.
The auction system is the main selling system in Australia. Mills located in wool growing areas also find that buying wool through private treaty arrangments is a very efficient system.
Mills will also use the futures market to hedge their risk either through the Sydney Futures Exchange or Macquarie Bank.
The on-shore topmaker looks forward to the implemation of sale by description and electronic selling. This will have cost saving implications to growers and top-makers.

## Slide 11: Demand from Spinner
fashion / consumers
  comfort, coloured fibres
competition
  other topmakers
  specialities
markets
  economic performance
spinner’s specifications (next)
Michael Blake
Notes: Written by: Michael Blake, Chargeurs Wool Eurasia.
Demand from the spinner to supply tops of any given specification depends on several things.
Consumers influenced by such things as magazines and advertisements wish to purchase apparel items with certain qualities such as lightweight, fine and comfortable. In order to meet the demand from further up the processing chain (weaver/garment maker), the spinner issues top specifications that will meet these needs.
Either the topmaker can or cannot meet the spinner’s specification. The topmaker is inhibited by the supply of particular wools and the constraints of the mill’s equipment to process to the required specifications.
Competition between topmakers creates a level playing field internationally, however some topmakers may specialise in a particular product.
The economic performance of consumer markets effects demand e.g. the Korean market completely collapsed in 1998. When export markets disappear, demand falls. Recently topmakers have suffered from the import quotas to China and that market is now not working, although this situation may ease long-term with the inclusion of China in the World Trade Organisation (WTO). Any sign of recession in an economy is a good forward indicator of a slow down in apparel sales.
Spinners’ specifications are covered in more detail in the next slides.

## Slide 12: Worsted Spinning
Source: Stanton, J. (1998)
Nm = m/g
yarn count
  linear density
2/56 Nm
  2 ply
  56 m/g count
Fibre diameter (µm)
Fibre length (mm)
Notes: Written by: Michael Blake, Chargeurs Wool Eurasia.
Source: Stanton, J (1998) Derived Demand for Raw Wool, Wool Marketing lecture series, CRC for Premium Quality Wool.
An indication of the fibre length and fibre diameter requirements for tops to achieve a given count are shown in this slide.
Explanation of terms:
Nm - Numero Metric (units metres per gram), yarn count (linear density) measure e.g. 2/56Nm means that a 2 ply yarn is the product, each ply yarn with a count (linear density) of 56 metres per gram (Nm).
The slide shows that a range of average fibre diameter and average fibre length in the top can achieve similar yarn products.
The fibre diameter required to make a yarn with a count of 56Nm would be finer than that required to make a yarn of 32Nm, given the same number of fibres in the final yarn X-section (~40). This is usually the case, since spinners want to maximise their output, with the lowest stoppages.

## Slide 13: Assembling Demand
Source: Stanton and Coss (1995)
Lambswool
Knitting yarn
Worsted
knitting yarn
Woollen knitting yarns
Wool/Polyester
worsted yarn
Plain worsted
weaving yarns
High twist
weaving yarns
(crepe)
95
90
85
80
75
70
65
60
55
50
45
18
19
20
21
22
23
24
25
26
27
28
95
Fibre diameter (µm)
Fibre length (mm)
Notes: Written by: Michael Blake, Chargeurs Wool Eurasia.
Source: Stanton and Coss (1995)
This slide further demonstrates that the demand for wool with certain length and diameter specifications is heterogeneous. Raw wool can go to several markets and it is difficult to identify exactly which markets it ends up in. For example, a 22mm wool top with an average length of 65mm may end up in plain worsted yarns, the wool/polyester blend market, or the woollen knitting market.
The slide shows the length/diameter requirements of a wool top destined for a particular end use.
Crepe yarns require the highest strength possible, since they are usually used as singles yarn. They are also highly twisted. A high Hauteur (average fibre length in top) is needed for high twist and high yarn strength.
Plain worsted weaving yarns are versatile, comprising the centre of the market in this slide, corresponding to about 22mm and 70mm. This is probably the major market.
Wool/polyester worsted yarn is made to meet price points for the blend market, so shorter wool at any diameter would be used for these yarns.
If the wool used in worsted knitting yarns is too long, fabric elasticity suffers. Lower average fibre length also contributes to yarn bulk which is desirable in knitted products. Fine diameter is a desirable attribute for these yarns.
Woollen knitting yarn usually utilises shorter and coarser raw material. The length can be down to about 50mm.
Lambswool knitting yarns are made from lambs’ wool, which is by nature, short and fine.
In general, knitting yarns tend to be length insensitive and have shorter fibre lengths than woven yarns. A worsted yarn would have longer fibre length than a woollen knitting yarn because of the nature of the processing system used.
Wools with an average staple length under 50mm are not processed on the worsted system. Short wools are processed on the woollen system.

## Slide 14: Spinners’ Specifications
Source: Blake, M. (1997)
Notes: Written by: Michael Blake, Chargeurs Wool Eurasia.
Source: Blake, M. (1997), The Customers of the Wool Industry - The Topmaker, Access to the Experts Wool Marketing module, CRC for PQW.
This slide shows in detail two examples of Spinners’ Specifications for 18.5m and 21.5m tops. Not only is fibre diameter and Hauteur defined, but there are the variables of Coefficient of Variation (CV) of diameter and CV Hauteur to contend with, complicated by the limitations on short fibre content, long fibres, shive, burr, colour, coloured fibre content, neps and ash content or dust.
The industrial aspect of top size, top format, sliver weight and evenness, oil content, and bale weight must also be controlled.
These technical requirements are agreed to and correlated between topmakers and spinners, and can be tested with a reasonable degree of accuracy. Therefore both parties can be satisfied that a quality product is produced and supplied.
The following technical requirements have established (IWTO Blue Book) procedures:
  micron
  Hauteur
  oil content
  sliver weight
  evenness
NB the statistical tolerance of the test methods are generally higher than the clients specifications.

## Slide 15: Wool Top Requirements
fibre related
micron
Hauteur
CVH
short fibre content
colour
coloured fibres
contamination
VM
style
repeatability
technical / industrial
oil content
sliver weight
VM content
top colour
final form
  bobbins
  bumps
Michael Blake
Notes: Written by: Michael Blake, Chargeurs Wool Eurasia.
A spinner calls for a particular type of top depending on the yarn he is making e.g. a typical standard worsted yarn would be a 2/48 Nm yarn requiring a top of 22m, 70mm Hauteur. The spinner will accept a top that is finer and longer (within reason) than that specificed, but will not accept one that is coarser and shorter because the yarn required can’t be achieved.
Diameter and length are important fibre related properties, as previously discussed. Coefficient of variation of Hauteur (CVH) is becoming less important as more research on its implications to spinning performance comes to light. However a CVH of say 55% would be a disaster, a CVH of approximately 45% or less is the figure often quoted on spinning specifications. The shape of the distribution of Hauteur fibre length is most important, as this indicates the spread of the fibre lengths within the top and gives a good indication of the amount of short fibre present. A top with too many short fibres will give problems during spinning. A shape like a camels hump with two different fibre length populations would be viewed unfavourably.
Colour is generally not a problem for Australian wool, however if the yarn is to go into a pastel or white fabric then a very white top may be requested. The colour of wool held in a stockpile will deteriorate over time but this may take many years.
Coloured fibres should not be a problem if the correct clip preparation has been carried out. The presence of contamination and/or coloured fibres greatly affects the value of the top and unfortunately if they are in the consignment it is not possible to detect them until the top stage. A top with contamination is a topmakers nightmare.
VM content is controllable. The type of VM being more of a problem than the total VM content. Seed, barley grass and shive become fibrous and are difficult to remove during processing.
The technical requirements in the spinner specifications are industrially linked and are very much determined by machine settings and operator expertise.

## Slide 16: Challenges in Commercial Topmaking
Michael Blake
1. JIT requirement
2. Competition
3. Market Risk
4. Price fluctuations
5. Keeping up to Technology
6. Raw Wool Specification
7. Contamination
Notes: Written by: Michael Blake, Chargeurs Wool Eurasia.
1. Customer requirement vs Wool availability
A major challenge to the topmaker is the ‘Just in Time’ philosophy where the customer doesn’t hold vast stocks but relies on being able to re-order the same product for delivery at short notice. Since wool supply is affected by seasonality, and processing to top takes time, the topmaker must make arrangments for such eventualities.
2. Competition
Customers are not loyal to one topmaker. They will go where the price and quality is right. The topmaker must stay one step ahead of their competition.
3. Market risk
If the export market fails the topmaker is left with top and/or awaiting payment.
4. Wool Price fluctuations
This is probably the largest financial challenge influenced by supply in the market. Factors such as long-term contracts and sanctity of contracts create price risk.
5. New technologies
The adoption of these allow the topmaker to keep ahead of competitors but it must be balanced against buying costs and costs of production. The handling of technical difficulties is also important.
6. Difficulty of predictability of a natural fibre
The effects of drought and seasonal changes can influence supply. Poorly prepared clips, or wools which do not meet specifications are a topmakers greatest nightmare.
7. Contamination
This is an area of great concern to the topmaker and the later stage processors. This is caused by poor on-farm quality controls, bale contamination, and coloured or stained fibres.

## Slide 17: Increasing Processor Demand
Michael Blake
promotion / R&D
selling out of season / edge of season
forward selling (direct to processor)
QA programs
additional measurement
  good strength and length
reduce delivery costs
  farm gate to mill
Notes: Written by: Michael Blake, Chargeurs Wool Eurasia.
There are a number of things that woolgrowers can do to increase processor demand.
Promotion of woollen products and wool blend products can show the versatility of the fibre, and make the consumer aware of the benefits of wool
Research and Development (e.g. wool jeans, wool/lycra, Colana, wool/cotton blends) will increase demand. Some of this work could be funded from royalties from spinners and weavers for using the Woolmark.
Smart woolgrowers can sell out-of-season or edge-of-season, which may achieve higher prices if particular wool types are in demand. The processors ideal situation is an even supply of wool types all year round.
Growers can command a premium by forward selling wool in high demand to processors. The benefits flow from minimal stockholding and low finance. Each sector, including processor needs to minimise risk in case of price increases or decreases.
Quality assurance programs should be integral to the industry. Clean clips mean good processing performance. Contamination can cause enormous losses in product value. The use of non contaminating packaging is being introduced after many years of feedback.
All wools should be additionally measured. The greatest benefit for a topmaker is when 90- 99% of wool is tested. This will definitely increase the precision of Hauteur prediction.
Selling costs can be reduced by Sale by Description, centralised selling (but decentralised storage), heavier bales, or selling directly to processor.

## Slide 18: Major References
Stanton, J. & Senior, A. (1994), Wool Market Awareness, Curtin University
Blake, M. (1997), The Customers of the Wool Industry - The Topmaker, Access to the Experts Wool Marketing module, CRC for PQW
Blake, M. (1998), Demand: A Processor’s Perspective, Wool Marketing lecture series, CRC for PQW