## Slide 1: Handle
Produced for the CRC for Premium Quality Wool undergraduate program by;
Dr. Brad Crook, The University of New England.
Notes: <number>
<footer>
This module introduces the concept of handle, this being the tactile properties of wool fibre. The role of fibre diameter and fibre curvature or crimp in determining handle is discussed. The relationship between diameter and curvature (crimp) is also shown.
Produced for the CRC for Premium Quality Wool undergraduate program by Dr. Brad Crook, The University of New England.

## Slide 2: Handle
Texture
Compression
Brad Crook
Source: Stevens (1994)
MAJOR
  mean diameter
MINOR
  diameter variation
  fibre damage
  fibre surface
  crimp
  grease, dust, VM
MAJOR
  crimp frequency
MINOR
  mean diameter
  grease
  staple pliability (crimp definition)
Notes: <number>
<footer>
Written by: Dr. Brad Crook, The University of New England.
Handle is a term used to describe the tactile aspects of fibre and fabric. It has both textural and compressional components. Fibre diameter exerts a strong influence on the textural properties of the fibre whereas crimp frequency (and fibre curvature) exert a strong influence on the compressional properties of the fibre. Handle is, therefore, in part a function of diameter and crimp.
Reference: Stevens, D. (1994). In “WOOLSPEC94: Specification of Australian Wool and its Implications for Marketing and Processing”. CSIRO Division of Wool Technology, H1.

## Slide 3: Handle: a function of diameter and curvature
Softer than average
Harsher than average
Brad Crook
Source: Stevens (1994)
Notes: <number>
<footer>
Written by: Dr. Brad Crook, The University of New England.
Source: Stevens, D. (1994). In “WOOLSPEC94: Specification of Australian Wool and its Implications for Marketing and Processing”. CSIRO Division of Wool Technology, H1.
Within a mob of sheep, finer fleeces tend to feel softer than higher diameter fleeces. At the same diameter, lower crimp frequencies tend to give a softer handle compared to higher crimp frequencies. On this basis, the preferred combination from a handle point of view would be low micron and low crimp (curvature). However, there is a trend for increasing crimp frequency with decreasing diameter within a flock.
A. The relationship between fibre diameter and crimp curvature in fine and medium wools;
B. The expected spread in handle scores if softness were due to diameter alone;
C. The expected spread in handle scores if softness were due to crimp alone;
D. The actual spread in handle scores.

## Slide 4: Handle: a function of diameter and curvature
Brad Crook
Source: Stevens (1994)
Notes: <number>
<footer>
Written by: Dr. Brad Crook, The University of New England.
Source: Stevens, D. (1994). In “WOOLSPEC94: Specification of Australian Wool and its Implications for Marketing and Processing”. CSIRO Division of Wool Technology, H1.
Within a mob of sheep, finer fleeces tend to feel softer than higher diameter fleeces. At the same diameter, lower crimp frequencies tend to give a softer handle compared to higher crimp frequencies. On this basis, the preferred combination from a handle point of view would be low micron and low crimp (curvature). However, there is a trend for increasing crimp frequency with decreasing diameter within a flock.

## Slide 5
Brad Crook
Notes: <number>
<footer>
Written by: Dr. Brad Crook, The University of New England.
The influence of fibre diameter and fibre crimp on wool handle can best be explained by considering a coiled spring. Taking the first two springs in this figure, they are of similar levels of coiling, but one is of finer diameter than the other. This spring would require less force to compress it. Comparing the second and third springs, which are of similar diameter, the second one has fewer turns in the coil. This will allow it to be more easily compressed than the third spring.
So at similar levels of fibre crimp, finer fibres are more easily compressed. And at similar fibre diameters, lower crimped fibres are more easily compressed. Thus having finer diameter and lower crimp should confer improved handle to the wool. As a general trend, though, fibre crimp increases as fibre diameter decreases. So the “softer than average” individuals are those who go against the trend, by having a level of crimp lower than expected given their diameter.