## Slide 1: Coarse Edge Defined
Produced for the CRC for Premium Quality Wool undergraduate program by;
Dr. Brad Crook, The University of New England.
Notes: <number>
<footer>
This module defines the coarse edge or prickle factor and shows how this trait relates to average fibre diameter.
Produced for the CRC for Premium Quality Wool undergraduate program by Dr. Brad Crook, The University of New England.

## Slide 2: “Coarse edge” and “Prickle Factor”
Brad Crook
“prickle” is the mechanical irritation caused by a fabric worn against the skin
not wool specific
“prickle” perceived when  5% of fibres exceed 30 µm but depends on a range of factors
Notes: <number>
<footer>
Written by: Dr. Brad Crook, The University of New England.
“Prickle” has been shown to be caused by mechanical irritation of the skin, when fabrics are worn next to the skin. Only a very small proportion of the population experience an allergic reaction to wool.
When fibre ends, protruding from the fabric surface, come in contact with the skin, there are two possible outcomes. The fibre end can either deflect away from the skin surface, or it can press into the skin surface. The latter scenario activates pain receptors in the skin, which are interpreted as a prickle sensation. The main determinant of whether the fibre end deflects or not is the diameter of the fibre. Thus prickle is not a wool-specific phenomenon, but is more closely associated with wool due to comparative diameters of wool, cotton and synthetics.
Research has shown that prickle arises when a fabric, worn next to the skin, has around 5% or more of fibres exceeding 30 microns. These coarser fibres show less tendency to deflect away from the skin surface. This proportion of coarse fibres is commonly referred to as the “coarse edge” of the diameter distribution. It should be noted, though, that many factors such as fabric construction and finishing techniques influence the actual threshold of coarse fibres required to generate prickle.

## Slide 3: Flock average MFD vs % of ewes with 5% or more fibres >30 microns
Brad Crook
Source: Crook, Piper and Mayo (unpub.)
0
10
20
30
40
50
60
70
80
17
18
19
20
21
22
23
24
Average fibre diameter
% ewes with 5% or
more fibres >30 µm
76%
4%
Notes: <number>
<footer>
Written by: Dr. Brad Crook, The University of New England.
As the average diameter of the flock increases, so too does the % of sheep within the flock that have 5% or more of fibres exceeding 30 micron. When the flock average diameter exceeds 21 micron, the % of sheep in the flock with “coarse edge” of 5% or more increases rapidly and exponentially.
Likewise, within a flock, the % of fibres in the fleece exceeding 30 microns rapidly increases once the fleece diameter exceeds 21 microns.
The higher the micron of the fleece or the flock, the greater is the likelihood of high coarse edge.