## Slide 1: Effluent Treatment
Produced for the CRC for Premium Quality Wool undergraduate program by;
Dr. Jock Christoe, CSIRO Textile and Fibre Technology.
Notes: This module examines the problems caused by scouring effluents. It goes on to describe solutions developed by CSIRO Division of Textile & Fibre Technology, formerly Wool Technology.
Produced for the CRC for Premium Quality Wool undergraduate program by Dr. Jock Christoe, CSIRO Textile and Fibre Technology.

## Slide 2: Effluent Characteristics
Wool wax 0.4 - 1.0 %
Suint 0.4 - 0.6 %
Dirt 0.4 - 1.2 %
Detergent 0.04 - 0.06%
J. Christoe
Notes: <number>
<footer>
Written by: Dr. Jock Christoe, CSIRO Textile and Fibre Technology.
Dealing with the effluent that results from the scouring of wool provides one of the biggest problems facing the wool processor.
Virtually every method for treating industrial wastewater has been tried with wool scouring effluents. Methods currently being used around the world range from doing nothing to complete incineration.
The components of a typical scour effluent are listed in this slide. Apart from the wool wax that is recovered by centrifuging, and sludge recovered in the contaminant recovery loops, all the contaminants removed from the raw wool end up in the effluent discharged from the scouring plant.
For a typical wool scour processing about 1500 kg raw wool per hour, this means that about 140 kg wool wax, 140 kg dirt and 70 kg suint are discharged hourly.

## Slide 3: Environmental Concerns
Organic load (mainly wax)
  1 scour = 30,000 people
Biorefractory nature of wax
  doesn’t degrade easily
Pesticide residues
  within limits in Australia
Detergent residues
  biodegradable alternatives available
Potassium levels
  potential source of fertiliser
J. Christoe
Notes: <number>
<footer>
Written by: Dr. Jock Christoe, CSIRO Textile and Fibre Technology.
The organic load from a typical wool scouring line (two metres wide) is equivalent to a population of 30,000 people. This obviously would put a severe strain on the sewerage treatment plants in nearly every Australian town and city. Most of the organic load comes from the wool wax.
A further difficulty encountered with scouring effluents is that the wool wax is very difficult to degrade by biological microorganisms, because of both its chemical structure and its physical characteristics.
Pesticides are applied to wool on the farm to control various sheep parasites. The type of pesticide and the amount found in the effluent depends upon the nature of the parasite and the time of treatment in relation to the time of harvesting of the wool. The concentrations found in the effluents are mostly within discharge limits for Australian wools.
The most common detergent used to wash wool in Australia is an alkylphenol ethoxylate nonionic detergent. When the detergent is biodegraded one of the by-products is alkylphenol. This chemical can be highly toxic to some species. Biodegradable alternatives that are not based upon alkylphenol are now available.
Potassium is an important nutrient. Suint contains about 25% potassium by weight. This suggests that treated scouring effluents should be beneficial when applied to the land. Experience with some wool scourers who have disposed of their treated effluents on the land has shown that you can have too much of a good thing. CSIRO calculations show that about 1000 ha are needed to dispose of the effluent from a single line in an environmentally sustainable way.

## Slide 4: Conventional Approach
Desuint
Scouring
Rinsing
Recovery
Loops
strong flow
rinse water
desuint
wool wax
sludge
wastewater treatment
J. Christoe
Notes: <number>
<footer>
Written by: Dr. Jock Christoe, CSIRO Textile and Fibre Technology.
A feature of current waste treatment practice is that the various aqueous discharges are combined and discharged from the scouring plant with or without further treatment.
Only a proportion of the wool wax and dirt (about 30%) is recovered in the recovery loops that continually treat the scouring liquors before returning them to the scour. The remaining contaminants are discharged from the scour as a wastewater.
This wastewater consists of two, or three, main effluent streams from the wool scour, namely a strong flow, a rinse water flow and a flow from a desuint bowl (if one is being used).
The strong flow consists of discharges from the dirt and wax recovery loops, and the centrate flowdown from the primary grease centrifuge.
For a typical wool scour processing about 1500 kg raw wool per hour, this means that about 140 kg wool wax, 140 kg dirt and 70 kg suint are discharged hourly. In addition a sludge containing about 45% solids is discharged to landfill (about 7 tonnes per day).

## Slide 5: Sirolan -SWIMS
Desuint
Scouring
Rinsing
rinse
water
wool wax
CF
Bio
Mem
PE
Recovery Loops
suint
flowdown
sludge
strong
flow
Potassium
fertiliser
back wash
Recyclable
sludge
Clean
wastewater
J. Christoe
Notes: <number>
<footer>
Written by: Dr. Jock Christoe, CSIRO Textile and Fibre Technology.
This overhead shows an overview of the CSIRO Scour Waste Integrated Management System (SWIMS).
Compared to the conventional approach to effluent treatment there are three clear differences. First, there is no sludge discharge from the contaminant recovery loops (the sludge is treated along with the strong flow).
Second, there is only one sludge produced.
Thirdly, the different aqueous streams are treated separately.
The final discharges from the system are:
(1) a resource, such as compost or a fuel supplement, made from the sludges produced by the wastewater treatment modules.
(2) a fertiliser concentrate rich in potassium
(3) a treated effluent, the composition of which depends on the technologies used to treat the strong flow.
If the CF effluent which now contains only water-soluble material is mixed with the desuint flowdown, there would be no aqueous effluent.

## Slide 6: Features of SWIMS
Resource rather than waste
  soil conditioning, nutrition
Integration with scouring process
  optimisation of return streams
Separation of waste streams
  technologies to suit content
One sludge
Modular Configuration
Flexibility
J. Christoe
Notes: <number>
<footer>
Written by: Dr. Jock Christoe, CSIRO Textile and Fibre Technology.
Sirolan SWIMS has the following important features:
The scouring wastes are considered to be a resource. By applying the principles of waste minimisation (reduce, reuse, recycle) to wool scouring we want to achieve a paradigm shift in the attitude of the scouring industry to waste management. Scouring effluents contain potassium and emulsified wool wax. The former is an important nutrient for plant growth, whereas the latter contains substantial proportions of complex steroids. Sludges produced through wastewater treatment could be useful soil conditioning agents and provide some nutritive value depending on their composition
Effluent treatment is closely integrated with the operation of the scouring line. The performance of the contaminant recovery loops must be optimised to produce concentrates containing as much of the contaminants as possible in the smallest possible volume. This reduces the cost of effluent treatment. Recycling treated wastewater to the scour is an important feature of the system. This allows for a reduction in water use and a possible improvement in productivity and wool quality because the wool is being processed in cleaner scouring liquors.
Each waste stream is treated separately. Rather than treating the combined scouring effluent, CSIRO believe that because the three streams have different characteristics they require different technologies for optimal treatment. The strong flow, as its name implies, contains the bulk of the pollution load. The rinse water contains low concentrations of contaminants. The desuint flowdown contains comparatively high concentrations of suint, and hence potassium, but very little wool wax.
A practical advantage of Sirolan SWIMS is that only one sludge is produced, no matter how many modules are used. This simplifies the whole process.
The wastewater treatment systems are modular. This means that the scourer can select those technologies that are appropriate to the local situation. If the situation changes, for example, water costs increase or sewer disposal charges increase substantially, then other modules can be installed to meet the new environmental requirements. This makes the system very flexible thus enabling the wool processor to choose the most appropriate system at a particular point in time.

## Slide 7: Sirolan CF
Commercialised module
Strong flow treatment
Chemical flocculation
  in-line process
  pH control
  polymeric flocculent
J. Christoe
Notes: <number>
<footer>
Written by: Dr. Jock Christoe, CSIRO Textile and Fibre Technology.
Sirolan CF is the first of the SWIMS wastewater treatment modules to be commercialised. It is a chemical flocculation process which has been specifically developed to treat the strong flow effluent, namely the combined flowdowns from the scouring bowls and contaminant recovery loops.
In contrast to the conventional chemical treatments, Sirolan CF is an in-line process, where the only chemicals used are an acid for pH adjustment and a polymeric flocculent. The choice of flocculent is crucial and very few of the many that were investigated were suitable. There are no mixing or settling tanks in the system other than a tank at the start of the process to balance the various flows that constitute the feed.
Sirolan CF has been licensed to ICI Watercare for its use in Australia and New Zealand.
The first commercial Sirolan CF plant has been operating at Thomas Chadwick and Son in England since July 1996.

## Slide 8: Typical Results for Sirolan CF
Concentration (%)
BOD
TS
SE
PS
SS
(mg/l)
  Feed
4.8
1.0
3.1
3.5
11000
Centrate
1.1
0.04
0.13
0.03
2800
Sludge
60.0
18.0
42.0
Efficiency (%)
96
96
99
75
J. Christoe
Notes: <number>
<footer>
Written by: Dr. Jock Christoe, CSIRO Textile and Fibre Technology.
Legend:
TS - total solids
SE - solvent extractable
PS - particulate solids
SS - Suspended solids
BOD - Biological Oxygen Demand
Removal efficiencies for wool wax and suspended solids averaged better than 95% in the full-scale evaluation trials.
The removal of total organic matter as shown by the Biological Oxygen Demand (BOD) was about 75%. The remaining BOD came from soluble organic matter which is not removed by the process. Trials from a half full-scale plant operating over a long time period, have produced a consistently high quality effluent.
Because SIROLAN CF removes virtually all the wool wax and particulate matter from the scouring effluent we believe that it is an essential pre-treatment for all scouring effluent treatments.
Subsequent secondary or tertiary treatments are significantly simplified by the removal of the contaminants responsible for the effluent being so difficult to treat. For example, membrane processes would encounter less fouling problems; biological treatments would not have to deal with the comparatively biorefractory wool wax; and physical treatments, such as evaporation, would not have the same extent of surface fouling on heat exchanger surfaces. The technology used in this second stage would depend upon the level of treatment that is wanted.
CSIRO have carried out extensive pilot plant studies using an aerobic biological method. The BOD can be easily reduced to below 200 mg/l by the treatment.

## Slide 9: Benefits of Sirolan CF
Simplicity
  in-line process
  only one sludge
Flocculent
  no Fe and Al cations
Sludge characteristics
  60% solid
Footprint
  small
J. Christoe
Notes: <number>
<footer>
Written by: Dr. Jock Christoe, CSIRO Textile and Fibre Technology.
Sirolan CF offers a number of advantages. These include:
Simplicity - We have developed an in-line treatment process. This simplifies the control of the process and reduces the number of treatment steps.
Costs - Because the design is simple we believe that the capital costs will be comparatively low. Our provisional cost estimates suggest that the operating costs will also be low.
Flocculent - No inorganic coagulants are used to destabilise the scouring emulsion. This means that the sludges do not contain undesirable cations such as iron and aluminium.
Sludge - The pilot plant trials suggest that the characteristics of the sludge are more suited to further treatment and cause less erosion in the decanter centrifuges used to dewater the sludge. The solids content of the sludge is about 60% compared to about 40% for other chemical sludges. Any sludges produced in the other modules comprising Sirolan SWIMS are mixed with the strong flow so that only one sludge is produced.
Footprint - Because the system is in-line the footprint is very small. The decanter and the polymer mixing station occupy the largest area.
Sirolan SWIMS offers the prospects of low water consumption through recycling of the treated water back to the scour as well as converting the wastes into valuable resources.
The adoption of Sirolan SWIMS means that environmental constraints are no longer a limiting factor on the location of a wool scour .