## Slide 1: Fibre / Pin Interaction in Carding
Produced for the CRC for Premium Quality Wool undergraduate program by;
Dr. Peter Auer, The University of New South Wales.
Notes: This modules examines the possibilities for fibre / pin interaction through a typical carding set consisting of a cylinder (or swift), a worker and a stripper.
The three basic carding actions are decided by the direction of the pins and the relative motion of the rollers. For more information see the “Carding Principles” module.
It should be noted that the final fibre movement is also dependent on such things as:
  fibre configuration (i.e. the fibre may be straight or hooked)
  fibre location (i.e. the fibre may be sitting down in the pins)
  fibre properties such as length
  pin density and condition
  relative roller speeds
  clearances between rollers.
This module shows how fibres move and how the fibre configuration can be altered by the carding unit.
Produced for the CRC for Premium Quality Wool undergraduate program by Dr. Peter Auer, The University of New South Wales.

## Slide 2: Carding Unit
Cylinder (C)
Worker (W)
Stripper (S)
C
S
W
a
b
c
Vc > Vs > Vw
Peter Auer
Notes: Written by: Dr. Peter Auer, The University of New South Wales.
This slide begins to describe the path of three fibres designated “a”, “b” and “c” as they move through the carding unit.
The carding unit (cylinder (C) (also known as swift), worker (W), stripper (S)) is repeated a number of times throughout the card. At each repeat similar fibre movement and fibre/pin interactions occur. The relative speeds and directions of rollers and pins are shown in this slide. This configuration is standard for any carding unit.

## Slide 3: Possibilities for fibre “a”
Vc > Vs > Vw
C
S
W
a
Peter Auer
Notes: Written by: Dr. Peter Auer, The University of New South Wales.
Fibre “a” is straight and set low in the pins, therefore there is a fair possibility that on this particular pass, this fibre will not undergo any fibre/pin interaction. It is likely to pass beneath the pins of the worker roller and stay on the cylinder.

## Slide 4: Possible movement for fibre “b”
C
S
W
b
1
2
3
4
5
6
8
7
9
10
11
1 of 3 slides
Peter Auer
Notes: Written by: Dr. Peter Auer, The University of New South Wales.
Fibre “b” has a leading hook. This means that the hook is at the front of the fibre as it is carried along by the cylinder.
Various positions are marked by numbers during the passage of this fibre through the carding unit.
At position 3 the fibre undergoes interaction between the points of the worker pins and the points of the cylinder pins (ie carding, point-to-point). It also wraps around the worker pins, and is transferred to the worker. Position 4 illustrates that before the fibre leaves the influence of the cylinder pins, it brushes past the fibre altering its configuration.
Position 5, 6 and 7 sees the fibre transported to the next fibre/pin interaction between the worker and the stripper. At position 8 the fibre is strippped off the worker by the stripper, and carried by the stripper to position 11.
So the fibre has been transported through the carding unit. Its configuration is the same (leading hook), but it is the opposite end which is now hooked. The fibre has been flipped around.

## Slide 5: Possible movement for fibre “b”
2 of 3 slides
C
S
W
11
12
13
14
15
path 1
Peter Auer
Notes: Written by: Dr. Peter Auer, The University of New South Wales.
There are a number of movements that might happen next. This slide shows the fibre being stripped off the stripper by the cylinder, and moving through positions 12 and 13, before undergoing the same change in configuration as before.
The fibre would then be transported by the worker through the stripper and back to the cylinder. This movement may not be automatic and the fibre may stay on either the worker or the stripper for a number of revolutions before being transferred.

## Slide 6: Possible movement for fibre “b”
C
S
W
path 2
11
12
13
14
15
3 of 3 slides
Peter Auer
Notes: Written by: Dr. Peter Auer, The University of New South Wales.
Alternatively, the fibre may avoid the influence of the worker again and continue on its path around the cylinder.
Remember that it is likely to undergo further fibre/pin interactions in other carding units.

## Slide 7: Possible movement for fibre “c”
C
S
W
1
2
3
4
5
6
c
Peter Auer
Notes: Written by: Dr. Peter Auer, The University of New South Wales.
Fibre “c” also has a leading hook. However, in this case at position 4 the fibre interacts with the pins of the worker, but is not trapped by them.
The fibre configuration has been changed, it now has a leading and a trailing hook, but the fibre moves onwards with the cylinder.
These examples should give an illustration of some of the interactions that can occur between fibres and pins during carding.