## Slide 1: Card Types
Produced for the CRC for Premium Quality Wool undergraduate program by;
Dr. Peter Auer, The University of New South Wales.
Notes: This module introduces the various types of cards used in fibre processing. Long staple card are of most interest, but hand carding and short staple carding are also featured.
Produced for the CRC for Premium Quality Wool undergraduate program by Dr. Peter Auer, The University of New South Wales.

## Slide 2: Hand carding
Peter Auer
Notes: Written by: Dr. Peter Auer, The University of New South Wales.
Hand carding was the original way that people separated and aligned fibres mechanically.
This is a step up from separating fibre with figers, however, all that is required to separate and align fibres is featured here.
There are two sets of pins or teeth. They are fixed to surfaces that can be moved past each other. This is enough to make a working point, ie point to point interaction occurs.
This is carding in its simplest form, but the transfer of this idea to more complex machinery took hundreds of years. The pins were finally mounted on rollers, converting linear motion to continuous circular motion. This form of mechanical carding is still with us today, and used for all staple fibres.

## Slide 3: Long staple Card
Swift
Peter Auer
Notes: Written by: Dr. Peter Auer, The University of New South Wales.
The diagram in ths slide shows the concept of working points on a card used to card long staple fibres. This design has proved itself over the years.
The working points are provided by smaller rotating rollers (workers) on the largest rotating roller (swift or cylinder). The smallest rollers in this grouping are called strippers which act to transfer fibres back to the swift. This grouping of rollers is called a carding unit, and is repeated throughout the card.
More information on card features can be found in the module “Worsted Card Features”. The interaction in the carding unit is covered in the module, “Carding Principles”.

## Slide 4: Typical Woollen Carding Set
Peter Auer
Source: Brearley, A., and Ireland J. A. (1981)
Notes: Written by: Dr. Peter Auer, The University of New South Wales.
Source: Brearley, A., and Ireland, J. A. (1981), “The Woollen Industry”, (WIRA: Leeds)
The diagram in this slide represents a long staple card used in the woollen industry.
In this slide we can see the same features, however in this case there are 5 swifts with 4 workers on each swift providing the working points.
This is required in the woollen system since all the fibre alignment is done on this machine in this processing system.
For more information about woollen processing see the “Processing on the Woollen System” module.

## Slide 5: Short staple Card
Peter Auer
Notes: Written by: Dr. Peter Auer, The University of New South Wales.
Finally this diagram shows a card used in processing of short staple fibres.
In this case, the working points are provided by “flats” moving over the main cylinder. This arrangement has been found to be suitable for short fibres but unsuitable for longer fibres.
Short staple cards generally run faster and with greater efficiency than long staple cards.