## Slide 1: A Fabric for the Future
Produced for the CRC for Premium Quality Wool undergraduate program by;
Dr. Barry Holcombe, CSIRO Textile & Fibre Technology.
Notes: A new fabric has been developed utilising the outstanding moisture absorbing properties of wool next-to-skin, and the functionality of polyester fibres in a continuous bi-component knitted fabric designed for the sportswear / activewear market.
Produced for the CRC for Premium Quality Wool undergraduate program by Dr. Barry Holcombe, CSIRO Textile & Fibre Technology.

## Slide 2: Comfort vs. Appearance
FR
appearance
comfort
KOR
JN
I
D
GB
USA
occasion/status
cut, finish, style
fabric/fibre quality
appearance retention
higher price
casual lifestyle
soft/smooth next to skin
competitive fibres (cotton)
separates, lower price
ALL CONSUMERS WANT
CLOTHES TO BE MORE COMFORTABLE
Barry Holcombe
Notes: <number>
<footer>
Written by: Dr. Barry Holcombe, CSIRO Textile & Fibre Technology.
Consumer trends over the last 20 years have seen an increase in preference for next-to-skin comfort. While national preferences vary, as illustrated in this slide, between appearance and comfort, it would be fair to say that all consumers want more comfortable clothing.
KOR - Korea
JN - Japan
I - Italy
FR - France
D - Germany
GB - Great Britain
USA - United States of America

## Slide 3: Clothing in the 90’s
FORMAL/TAILORED
CASUAL
SPORTSWEAR/ACTIVE
business/social
everyday/home
sports/leisure
suits
longcoats
skirts
dresses
sweaters
jackets
blazers
trousers
jeans
cords
blousons
anoraks
leggings
sweatshirts
light jackets
tracksuits
polo shirts
fleece jackets
Barry Holcombe
Notes: <number>
<footer>
Written by: Dr. Barry Holcombe, CSIRO Textile & Fibre Technology.
Other clothing trends have seen the traditional stronghold markets for wool products eroded, as casual and sports / active wear markets have increased. While all markets will continue to grow, these trends are projected to continue into the next century. The sports / active wear market is projected to experience the greatest relative growth.

## Slide 4: Factors in Trouser Comfort
0
10
20
30
% contribution
appearance
drape
thermophysiology
tactile
Barry Holcombe
Notes: <number>
<footer>
Written by: Dr. Barry Holcombe, CSIRO Textile & Fibre Technology.
Studies have shown that two factors contibuting nearly 40% to trouser comfort are tactile and thermophysiological properties. Thermophysiological properties are also referred to as micro-climate control properties.

## Slide 5: Diameter and Tactile Appeal
19µm
21µm
23µm
w/PES
w/µfib
crisp
scratch
harsh
stiff
appeal
rating
WOMEN’S
TROUSERS
Barry Holcombe
Notes: <number>
<footer>
Written by: Dr. Barry Holcombe, CSIRO Textile & Fibre Technology.
Examining tactile appeal more closely, the conclusion can be drawn that finer fibre diameter contributes significantly to tactile appeal.
In this slide, finer fibres are less crisp, less scratchy, less harsh, less stiff, amd more appealing.

## Slide 6: Wool Fabric Tactile Ratings
Barry Holcombe
0
30
60
90
120
prickly
scratchy
itchy
smooth
soft
drapes
desirability
18.8µm
20.9µm
23.4µm
Notes: <number>
<footer>
Written by: Dr. Barry Holcombe, CSIRO Textile & Fibre Technology.
A similar scenario can be constructed from this slide.

## Slide 7: Summary
Consumer preferences
  comfortable clothing
    tactile appeal
    microclimate control
  clothing for many occasions
Tactile appeal
  important in consumer preferences
  fibre diameter is fundamental to tactile appeal
  finer wool fibres are better
  New fabrics must meet these needs
Barry Holcombe
Notes: Written by: Dr. Barry Holcombe, CSIRO Textile & Fibre Technology.
Consumers prefer comfortable clothing (with inherent tactile and microclimate control properties). Finer fibres are an inherent part of that tactile appeal.
New fabrics must meet these needs.

## Slide 8: What is ??
Two-layer composite construction
  new knitted technology
  superfine wool against the skin
  strongly wicking outer face
Both faces completely independent
Specific fabric finishing processes
Barry Holcombe
Notes: <number>
<footer>
Written by: Dr. Barry Holcombe, CSIRO Textile & Fibre Technology.
Sportwool™ is a two layer composite construction employing recently developed knitting technology. The fabric is constructed such that an inner layer of superfine wool ends up next-to-skin, while an outer layer of polyester fibre also acts to wick moisture away from the skin.
Whist the fabric is continuous, both faces are completely independent.
Specific finishing processes are used on the fabric to improve performance.

## Slide 9: is UNIQUE
Moisture management is the current focus in active sportswear market
provides
Natural fibre against skin
Two level moisture management
  controls microclimate humidity
  wicking gradient inside to outside
Barry Holcombe
Notes: <number>
<footer>
Written by: Dr. Barry Holcombe, CSIRO Textile & Fibre Technology.
To improve moisture management in active and sports situations, the wool fibre is able to firstly control microclimate humidity, while the inside to outside wicking gradient is a second moisture management device.

## Slide 10: Wicking Mechanism - 1
Barry Holcombe
Notes: <number>
<footer>
Written by: Dr. Barry Holcombe, CSIRO Textile & Fibre Technology.

## Slide 11: Wicking Mechanism - 2
Barry Holcombe
Notes: <number>
<footer>
Written by: Dr. Barry Holcombe, CSIRO Textile & Fibre Technology.

## Slide 12: Research to Identify Benefits
Trials in controlled climate
  elite athletes
  compared with polyester equivalent
    Coolmax TM
  subjective differentiation
Related activities measured
  physical measurement of microclimate
  physiological measurement
Barry Holcombe
Notes: <number>
<footer>
Written by: Dr. Barry Holcombe, CSIRO Textile & Fibre Technology.
Subjective trials in controlled climates using elite athletes have been conducted comparing the performance of Sportwool™ to the polyester competitor Coolmax™.
At the same time microclimate and physiological data were collected.

## Slide 13: Subjective Preference
0
10
20
30
damper
warmer
more clingy
more noticeable
more comfortable
average subjective rating
Coolmax is….. Wool is……...
elapsed time
Barry Holcombe
Notes: <number>
<footer>
Written by: Dr. Barry Holcombe, CSIRO Textile & Fibre Technology.
As far as subjective trials with elite athletes were concerned, Sportwool™ was judged better performed during the trial. The separation between the fabrics became greater as more time elapsed.

## Slide 14: Microclimate Humidity
elapsed time (min)
0
10
20
30
40
40
90
50
60
70
80
Coolmax
relative humidity %
Barry Holcombe
Notes: <number>
<footer>
Written by: Dr. Barry Holcombe, CSIRO Textile & Fibre Technology.
Measurements of micro-climate humidity showed that Sportwool™ outperformed Coolmax™ during the duration of the trial.

## Slide 15: Skin Microclimate Discomfort
minutes of exercise
sweating
starts
Coolmax
0
2
4
6
8
rate of vapour pressure increase
Barry Holcombe
Notes: <number>
<footer>
Written by: Dr. Barry Holcombe, CSIRO Textile & Fibre Technology.
After sweating had actually started, it could be seen that Sportwool™ again performed better as measured by the rate of vapour pressure increase (rate of humidity rise). This was especially the case in the critical time just after sweating started. Smaller fluctuations were also noted for Sportwool™.

## Slide 16: Research Outcomes
subjectively preferred
  less damp
  less clingy
  more comfortable
Microclimate humidity buffering
  lower rate of humidity rise
  smaller fluctuations
  SUPPORTED BY HARD SCIENTIFIC DATA
Barry Holcombe
Notes: <number>
<footer>
Written by: Dr. Barry Holcombe, CSIRO Textile & Fibre Technology.
Sportwool™ was subjectively preferred by the elite athletes, but also these preferences were reflected in the hard scientific data gathered during the trials. Essentially the microclimate buffering of Sportwool™ was better.

## Slide 17: Consumer Benefits
Cooler during exercise
Drier when sweating
Warmer in the cold
Natural moisture buffering
Pay-off for consumers is superior comfort in all conditions
Barry Holcombe
Notes: <number>
<footer>
Written by: Dr. Barry Holcombe, CSIRO Textile & Fibre Technology.
The consumer benefits from this new fabric because it is cooler during exercise, drier when sweating, warmer in the cold, and moisture at the skin level is buffered better.
Sportwool™ appears to offer superior comfort in all conditions.

## Slide 18: Flexible Technology
easy-care
wide weight range
appearance and handle can be tailored to end use
stretch fabric under development
socks already trialed
A fabric for many occasions
Barry Holcombe
Notes: <number>
<footer>
Written by: Dr. Barry Holcombe, CSIRO Textile & Fibre Technology.
Sportwool™ is a fabric for many occasions, offering easy care over a wide range of fabric weights. The appearance and handle can be tailored to different end-uses.
Other new products such as a stretch fabric version of the fabric are under development.

## Slide 19: Further Information
visit the website
http://www.sportwool.com
Barry Holcombe
Notes: Written by: Dr. Barry Holcombe, CSIRO Textile & Fibre Technology.