## Slide 1: Summary of Lecture 12: Chilling, Freezing & Boning
By Dr Mike North, AgResearch MIRINZ Centre, New Zealand

## Slide 2: Mechanisms for Heat Transfer
Conduction
Convection
Radiation

## Slide 3: What is Chilling and Freezing?
Chilling is the process of cooling a food while it remains above its freezing temperature. The temperature of the cooling medium (air or water, for instance) doesn't matter, as soon as the food starts to freeze, it can no longer be considered a chilling process.
Freezing is the process of removing heat from a food so that the water content of the food is converted into ice. A food starts to freeze when it is cooled to below its freezing temperature and is considered fully frozen when no more of the water in the food can be converted to ice.

## Slide 4: Predicting Chilling and Freezing Times
The prediction of chilling and freezing times for meat products is very important for design and optimisation of meat plant processes.
The cooling rate of the meat can also have a big impact on the tenderness and microbiological quality of the meat.
The course notes outline how to predict these for simple situations and tell you where to go for help with more complex problems.

## Slide 5: Heat Loads in Chilling and Freezing
Heat load describes the rate at which heat energy enters the cooling medium. The heat load may come from the food product or from some other source of energy such as fans, lights or warm air entering through an opening.
To maintain a constant temperature in a chiller or freezer, it is important that the refrigeration system is able to remove heat from the cooling medium at the same rate as it enters from the various heat sources in the cooler.
The course notes discuss the main sources of heat load in the meat chillers and freezers, and show you how to estimate some of these.

## Slide 6: Cold boning and Hot boning
Cold boning refers to the process of removing the meat from the bones and cutting the carcass down into smaller pieces after chilling (usually to below 7°C).
Hot boning refers to the process of removing the meat from the bones before any significant cooling occurs, it is called ‘hot boning’ because the product is still near to the body temperature of the animal.

## Slide 7: Advantages of hot and cold boning
Advantages of hot boning:
Lower refrigeration costs
Faster processing
Less inventory and lower capital costs for buildings
Less weight loss
Advantages of cold boning:
Meat retains characteristic shape
Easier to handle during boning
May not require electrical stimulation
Slaughter floor and boning room do not have to be synchronised