## Slide 1: Processing Technology I
Electrical inputs – electrical currents applied to the animal/carcase during meat processing operations

## Slide 2: Sheep meat processing
Electrical stunning
Carcase immobilisation
Electronic bleed rail stimulation
Electrical stimulation (ES) (meat quality)

## Slide 3: Beef processing
Carcase immobilisation
Electronic bleed rail stimulation/ES
Hide puller stiffening
Electrical stimulation (ES) (meat quality)

## Slide 4: Beef Immobilisation Electrodes.

## Slide 5: Beef Mid-Voltage Electrical Stimulation / Electronic Bleed

## Slide 6: Sheep Mid-Voltage Electrical Stimulation

## Slide 7: Electrical safety
Historically, electrical stimulation used very high (1000 V) dangerous voltages
Modern electrical inputs now use ‘safe’ mid-voltages
BUT Electricity must always be treated with respect

## Slide 8
+1100 V
-1100 V
0
+300 V
VOLTAGE COMPARISON BETWEEN OLD HIGH VOLTAGE STIMULATION
AND NEW MID VOLTAGE STIMULATION SYSTEMS
HV STIMULATION
MV STIMULATION

## Slide 9: Table 25.1 Summary of waveform parameters for mid-voltage electrical inputs.
Electrical input | Pulse width (msec) | Time between pulses (msec) | Frequency (Hz)
Carcase immobilisation | 0.1 | 0.4 | 2000
Bleed rail/ES | 0.5 | 200 | 5
Hide puller | 1 - 2 | 24 | 40
Electrical stimulation (ES) | 1 | 68 | 14 - 15

## Slide 10: Electrical inputs
Individually, they increase processing efficiency
Improve worker safety (immobilisation)
Increased blood for sale as co-product (bleed rail stimulation)
Reduced waste water contamination (bleed rail stimulation)
Prevent carcase and muscle damage (hide-puller)
Improved meat quality (prevent cold-shortening toughness)
Combined additive effect of all inputs
Can be disadvantageous if total combines input is excessive
– meat slightly tougher, drier.