## Slide 1: Water Sustainability
RSNR 421/521 - Topic 7
Andrew Boulton & Darren Ryder
Notes: Mr Chairman
Members of the Board
Ladies and Gentlemen

## Slide 2
Hydrological linkages occur vertically, laterally, and longitudinally
Linkages determine associations of wetlands, rivers and their catchments
Contribution of water via the different linkages govern the water regime
Some Slides to Augment the Lecture Material

## Slide 3
Linkages at a Catchment Scale

## Slide 4: Water Regime
Water regime is where, when, and to what extent water is present in a wetland
Alteration of natural water regimes is the highest priority issue in management of Australian waters. Impacts result from changes to the timing, frequency, duration, extent and depth, and variability in the availability of water
Most physical, chemical and biological processes in standing and running waters are controlled and constrained by the water regime and its components

## Slide 5: Water Regime
Three different rivers
with different water
regimes

## Slide 6: Global Aquatic Linkages
water travels vertically and horizontally, and exists in three different phases (gaseous, liquid, and solid)
continuous circulation of water occurs between the earth and the atmosphere, and is powered by gravity and solar energy
relative contributions of the linkages in the hydrological cycle change over time and across the earth, and together with human influences, these variations in the hydrological cycle are fundamental to the distribution and water regime of wetlands across the world's surface

## Slide 7
Global Aquatic Linkages

## Slide 8: Global Water Budget
Globally, some 119 000 km3 precipitation falls on land (less than one-third of the global surface) and 72 000 km3 returns by evaporation to the atmosphere
The difference eventually runs off as surface or groundwater
Evaporation from the oceans exceeds the precipitation that falls on them; this spatial "imbalance" in the hydrological cycle ensures the existence of lakes and rivers on the land

## Slide 9: Global Water Budget

## Slide 10: Water Resources in Australia
Australia is the driest inhabited continent. Two-thirds of the continent receives less than 500 mm of rain annually
Australia's continental surface drainage basins have been grouped into 12 drainage divisions, nine of which enter the sea (exorheic)
49% of mainland Australia either has no co-ordinated drainage (arheic) or the rivers drain to inland lakes (endorheic)

## Slide 11: Divertible Surface Water Resources
Defined as those of fresh water that could be economically developed

## Slide 12: Groundwater Resources
Groundwater is separately assessed in 61 "groundwater provinces"
Major sedimentary aquifers of variable water quality lie under some 60% of the continent, including the Great Artesian Basin
Historically, groundwater availability facilitated the spread of European settlement inland. In much of inland Australia, it is the most important water resource because it is more reliable and less prone to evaporation than the sparse surface waters

## Slide 13: Water Regimes and Aquatic Linkages
Effective management of water resources depends on understanding the ecological processes that occur in natural and constructed wetlands
In Australia, emphasis has shifted from concern largely about water quantity and supply for human needs (engineering solutions) to protecting water quality and sustaining natural aquatic ecosystems (ecological solutions)
Altering linkages often alters water regimes; the reverse is also true

## Slide 14: Water Regimes and Aquatic Linkages
Threats to water sustainability can be classified according to whether they stem from water regime issues or catchment inputs

## Slide 15: Draining and Damming Wetlands
What are the ecological effects of draining wetlands?

## Slide 16: River Regulation by Dams and Weirs
What are the ecological effects
of draining wetlands?
What are the ecological effects of dams and weirs?

## Slide 17: River Regulation by Dams and Weirs
River regulation alters:
flow regimes, including timing of discharge and the extent of inundation of the floodplain,
sediment regimes, including rates of deposition and erosion, channel morphology and nature of the bed sediments, and,
channel and floodplain integrity by disrupting the natural continuum of the river including fish and invertebrate migration upstream or out onto the floodplain.

## Slide 18: Complex Ecological Responses

## Slide 19: Environmental Flows
If most ecological impacts result from changes in flow regime, we must focus management efforts on restoring the regime to its natural state
Environmental flows are natural flows or releases of water intended to supply the environment's needs
Quantity, timing, volume and duration of the releases, and water quality are all critical aspects

## Slide 20: Catchment Issues - Salinisation
What are the ecological effects of wetland salinisation?

## Slide 21: Catchment Issues - Sedimentation
What are the ecological effects of sedimentation?

## Slide 22
Catchment Issues – Grazing and Riparian Zone Clearance
What are the ecological effects of grazing and
clearing of the riparian zone?

## Slide 23: Assessing Wetland and River Health
Wetland ‘health’ refers to its condition expressed in terms of a value system – if it is more ‘healthy’, then that is considered good
Benefits seen in human values and ecological values
Ecosystem goods and services – what are the benefits of sustainable water on the farm?

## Slide 24: Assessing Wetland and River Health

## Slide 25
Assessing Wetland and River Health
What are the benefits of biological indicators?

## Slide 26: Synthesis
Water sustainability can be assessed in terms of the persistence of its quantity and quality in a state that matches our needs and those of the environment. Human activities influence physical, chemical, and biological features of standing and running waters worldwide
To manage these effects, we must treat the causes not the symptoms. We need to understand how our water resources are linked and how impacting on one will often cause flow-on effects to another
Looking after the linkages and finding a balance between the water quality and quantity needed for farming and for the environment are challenges in the quest for sustainable water

## Slide 27: Synthesis – 5 Myths to Ponder
Water is a free good
Water can be managed in isolation
The desert can be made to bloom
Social values will not change
Water management is mainly a technical matter

## Slide 28: The End