## Slide 1: Alternative Shearing Practices
Topic 4 – Lecture 1
Notes: Mr Chairman
Members of the Board
Ladies and Gentlemen

## Slide 2: Traditional Shearing
Very little development since 1887 when mechanically driven shears were introduced
Increasing costs
Increasing shortage of skilled shearing labour

## Slide 3: Developments in Wool Harvesting
Bioclip
  Development started in the 1970’s by CSIRO
  Uses a natural protein to induce a break in the wool
ShearExpress
  Australian Wool Innovation initiative
  Sequential Production Line system
Robotic Shearing
  Developed during the 1970’s and 1980’s by UWA
  Research no longer continuing

## Slide 4: Bioclip
Sheep are vaccinated with natural protein
Fibre temporarily stops being produced after approximately 28 hours
New fibre reaches the skin after approximately 14 days
Wool is harvested after 28 days

## Slide 5: Bioclip
Netted Lamb
Harvested lamb
Source: BCS Agribusiness & The McKinnon Project (2002)

## Slide 6: Benefits of Biolcip
Improved animal health
Increased wool quality and value
Increased processing performance
Improved animal husbandry

## Slide 7: ShearExpress
Housed within a mobile, expandable B double trailer
7 specialised stations with defined blow patterns
Sheep travel along a conveyor system, held by leg cuffs and positioned by manipulator arms for each blow
Once removed, fleece is prepared, classed and tested if required
Target is 120 sheep per hour

## Slide 8: ShearExpress
Outside of ShearExpress
Inside of ShearExpress
Source: AWI (2002)

## Slide 9: Benefits of ShearExpress
Higher productivity in wool harvesting
Higher consistency of clip quality and preparation with less damage to fleeces
Improved Occupational Health and Safety and air-conditioned working conditions
Employment opportunities for rural areas
Reduced requirements for capital intensive infrastructure

## Slide 10: Robotic Shearing
Also referred to as Automated Mechanical Shearing (AMS)
UWA was successful in developing the Shear Magic robot and SLAMP (simplified loading and manipulation platform) to shear the entire sheep
Development stopped when industry entered a period of financial hardship in the early 1990s
Work has never recommenced

## Slide 11
End of Summary Slides
Close Window