## Slide 1: WOOL 372/472/572 Wool Biology/Metrology
Topic 5
Background to Wool Metrology
Peter Sommerville

## Slide 2: Learning Objectives
The history of wool metrology
The essential technical requirements of wool measurement systems
Understand the sources of variation within wool metrology systems
Procedures by which metrology standards are developed
Managing the technical limitations

## Slide 3: About Wool Metrology
What is Wool Metrology?
Why Measure Wool?
A Brief History of Raw Wool Metrology
The Measurable Quality Characteristics of Wool?
  Describing Wool
  What Can Be Measured?

## Slide 4: What is Wool Metrology?
Metrology is the science of measurement
Focussed upon developing (evaluating) technologies and systems for objectively measuring the quality attributes of raw materials and manufactured products

## Slide 5: Why Measure Wool?
Fitness for use
  Quality of Design
  Quality of Conformance
Quality Characteristics
  Physical
  Sensory
  Time Orientation
Variability

## Slide 6: A Brief History of Raw Wool Metrology
Daubenton (1777)
Formation of IWTO (1928)
Development of the Airflow Instrument
Core & Grab Sampling Systems
Australian Objective Measurement Program

## Slide 7: Measurable Quality Characteristics of Wool
Mean Fibre Diameter
Yield
Staple Characteristics
Colour
Bulk

## Slide 8: Technical Requirements of Metrology Systems – Basic Concepts
Sampling - the Number One Issue
Accuracy & Precision
Bias
Sensitivity
Detection Limit
Range
Selectivity

## Slide 9: Objective Criteria
TABLE 3.1: Objective Criteria for Evaluating Testing Systems | 
Criterion | Numerical Measure
1. Precision | Absolute Standard Deviation Relative Standard Deviation Coefficient of Variation Variance
2. Bias | Absolute Systematic Error Relative Systematic Error
3. Sensitivity | Calibration Sensitivity Analytical Sensitivity
4. Detection Limit | Blank plus 3 times the standard deviation of the blank
5. Range | Limit of quantitation (LOQ) to limit of linearity (LOL)
6. Selectivity | Coefficient of Selectivity
Source: P.J. Sommerville, Technical & Commercial Requirements of Wool Testing Systems, AWTA Ltd Newsletter, September 2001 | 

## Slide 10: Accuracy & Precision
Absolute Standard Deviation
Relative Standard Deviation
Standard Deviation of the Mean
Coefficient of Variation
Variance of the mean
Confidence Level (95%)

## Slide 11: BIAS
Random or indeterminate errors
Systematic or determinate errors
  Sampling
  Differences in fundamental assumptions
  Personal Errors
  Instrumental Errors
  Method Errors
  Interferences

## Slide 12: Accuracy, Precision & Bias

## Slide 13: Development of Standard Test Methods
The Role of IWTO
An Introduction to IWTO Specifications
Application of IWTO Test Specifications for Greasy Wool
On Farm Fibre Measurement
Future Developments

## Slide 14: Role of IWTO

## Slide 15: IWTO Specifications

## Slide 16: Technical Limitations of Wool Metrology Systems
Between-Core/Between-Grab Variation
Within-Laboratory Variation
Between-Laboratory Variation
Check Tests & Retests