## Slide 1: WOOL 372/472/572 Wool Biology/Metrology Topic 16 Fibre Diameter Measurement of Slivers and Tops Errol Wood
Notes: Mr Chairman
Members of the Board
Ladies and Gentlemen

## Slide 2: Instruments for fibre diameter testing
Projection microscope
  Manual method for calibrating other methods
Airflow
  Simple, now obsolete method
Optical Fibre Diameter Analyser (OFDA)
  Applies digital image processing technology
Laserscan
  Applies laser detection technology

## Slide 3: Relevant IWTO test methods for wool fibre diameter measurement
IWTO 6 - Projection Microscope
IWTO 12 – Laserscan
IWTO 47 - OFDA

## Slide 4: Projection Microscope
Snippet cutting

## Slide 5: Data from Projection Microscope
Class interval (μm) | Mid-point d (μm) | No. of snippets n | % of snippets F | d x n | d2 x n
0-2 | 1 | 0 | 0 | 0 | 0
2-4 | 3 | 0 | 0 | 0 | 0
4-6 | 5 | 0 | 0 | 0 | 0
6-8 | 7 | 0 | 0 | 0 | 0
8-10 | 9 | 0 | 0 | 0 | 0
10-12 | 11 | 2 | 0.05 | 22 | 242
12-14 | 13 | 23 | 0.575 | 299 | 3887
14-16 | 15 | 144 | 3.6 | 2160 | 32400
16-18 | 17 | 719 | 17.975 | 12223 | 207791
18-20 | 19 | 1365 | 34.125 | 25935 | 492765
20-22 | 21 | 997 | 24.925 | 20937 | 439677
22-24 | 23 | 380 | 9.5 | 8740 | 201020
24-26 | 25 | 197 | 4.925 | 4925 | 123125
26-28 | 27 | 92 | 2.3 | 2484 | 67068
28-30 | 29 | 53 | 1.325 | 1537 | 44573
30-32 | 31 | 19 | 0.475 | 589 | 18259
32-34 | 33 | 8 | 0.2 | 264 | 8712
34-36 | 35 | 1 | 0.025 | 35 | 1225
36-38 | 37 | 0 | 0 | 0 | 0
38-40 | 39 | 0 | 0 | 0 | 0
 | Totals | 4000 | 100 | 80150 | 1640744

## Slide 6: Fibre diameter distribution

## Slide 7: Calculations of key statistics
MFD =
Σ d x n
n
=
80150
4000
=
20.03 μm
(Σ n x d)2
Σ n
-
Σ n x d2
Σ n - 1
(80150)2
4000
-
1640744
4000 - 1
SD =
=
= 2.95 μm
SD
MFD
X 100 =
CVD =
2.95
20.03
X 100 = 14.7%

## Slide 8: OFDA slide preparation

## Slide 9: OFDA100 system

## Slide 10: Laserscan

## Slide 11: OFDA4000
A new instrument for measuring slivers/tops
Prepares beard of aligned fibres, then
Measures:
  Fibre length, curvature
  Fibre diameter statistics
  Comfort factor (fibre ends)
  Diameter profile along beard

## Slide 12: Thank you
Notes: Mr Chairman
Members of the Board
Ladies and Gentlemen