## Slide 1: Energy Utilisation and Conservation in Wool Scouring
Topic 13
Notes: Mr Chairman
Members of the Board
Ladies and Gentlemen

## Slide 2: Energy in wool scouring
Wool scouring is very energy intensive
Process requires heating of water and heat for drying
Driving motors, lighting etc, uses less energy
Electrical energy used mostly for motors, lighting, space heating
Fuel energy used to produce direct heat or steam

## Slide 3: Energy Management
Energy management should minimise the energy cost per unit of production (cents/kg)
It should ensure that energy is used efficiently
Also provide substitutes for expensive fuels
Energy management depends on
  Cooperation of all staff
  Sufficient funds to implement changes
  An efficient check on energy usage

## Slide 4: Aims of an energy management programme
Identify $ losses through energy waste
Recommend ways to reduce energy waste:
  Improved maintenance of plant, buildings
  Modifying existing plant and buildings
  Installing new plant
  Substituting existing fuels
  Instructing personnel on preventative maintenance and energy conservation
Needs firm, realistic goals with timetable
Regular checking of results, revise with experience

## Slide 5: Energy audit
First step in energy management programme
Examines plant to check if most suitable energy sources are being used, and efficiently used
Company records give data on energy consumption and costs
  Quantities and each form of energy
  Annual and seasonal trends
  Calculate energy coefficient - energy use per unit of output (expressed in cents/MJ)
Calculate theoretical minimum energy use to compare with actual energy use

## Slide 6: Standard energy coefficient
To calculate the standard (or low fuel) coefficient it is necessary to know:
  Fuel being used
  Best possible efficiency of plant, including
    An efficient boiler and steam distribution system
    An efficient wool dryer
Compare standard coefficient with present energy coefficient
If unacceptable a plant survey should highlight waste and inefficiencies
Implement energy conservation measures

## Slide 7: Energy conservation measures
Good housekeeping of existing plant (usually low cost)
Modifications to, or replacement of, plant (more costly measures)
Change to cheaper fuel. Alternatives include
  Coal
  Natural gas
  Waste wood from timber industry
  Mixture of oil and low quality woolgrease

## Slide 8: Good housekeeping areas
Storage of fuel
Boiler house
Steam distribution
Scouring train
Dryer

## Slide 9: Waste heat recovery
High temperature waste water and air has recoverable heat energy (~60% is possible)
Points to consider before implementing:
  Is existing process efficient?
  Perhaps improve efficiency of current system first
  Calculate amount of heat that can be recovered – is this amount worthwhile?
  Can recovered heat be usefully used?
  Can waste heat be used directly? No need to install costly heat recovery equipment

## Slide 10: Plate heat exchanger
Series of closely-spaced metal plates clamped together
Plates corrugated to improve rigidity and heat transfer
Two flows of fluid pass between alternate plates
Advantages:
  Compact and space saving
  Easily inspected and cleaned
  Made to variable capacities

## Slide 11: Dryer exhaust heat recovery
Wool dryer needs supply of hot air to replace air that is exhausted
Recover heat from exhaust – transferred to stream of fresh air entering dryer
As moisture content of air increases its ability to evaporate moisture decreases
Fresh air entering dryer
  Is warm as possible with little moisture, and
  Must be free from dust, fibre etc, so
  Shouldn’t mix with exhaust air

## Slide 12: Heat pipe heat exchanger (1)
Thermal recovery unit

## Slide 13: Heat pipe exchanger (2)
Bank of pipes, finned to improve heat exchange
Pipe is an evacuated tube with porous lining, partly filled with refrigerant and sealed
Heat exchange is indirect – refrigerant in heat pipes changes from liquid to vapour between cold and hot air streams
As vapour condenses to form liquid at cold end it gives up its heat to fresh cold air, warming it
Condensed liquid travels back to evaporating (warm) zone) by gravity or capillary action, to repeat cycle

## Slide 14: Heat pipe exchanger (3)
Interior of a single heat pipe

## Slide 15: Heat recovery system for dryer

## Slide 16
End of Summary Slides
Close Window