## Slide 1: Control and Instrumentation Systems for Wool Scouring
Topic 5
Notes: Mr Chairman
Members of the Board
Ladies and Gentlemen

## Slide 2: Requirements for modern wool scouring
Better quality control of scoured wool
Better efficiency – minimum usage of labour, water, energy, detergent, chemicals
Optimum productivity – highest possible production from plant and labour
Stringent effluent control

## Slide 3: Benefits of C&I technology
Helps reduce expenditure on labour, maintenance, energy, detergent, chemicals
Provides information to management for good decision making
Enables operators to be better informed on operating conditions
Helps to produce a more consistently scoured product
Many situations in plant where C&I useful
Modern systems use:
  electronic sensors to acquire information
  electric signals transmit information
  small electric motors to actuate control functions

## Slide 4: C&I Definitions
PROCESS CONTROL – manual or automatic control to maintain right conditions, give best result
PROCESS VARIABLE – any property that can change or vary
CONTROLLED VARIABLE – process variable to be controlled –e.g. temperature inside wool dryer
MANIPULATED VARIABLE – process variable to be altered by the controller to change the controlled variable – e.g. damper setting to change humidity inside dryer
LOAD VARIABLE – a variable part of the process that upset controlled variable – e.g. wool throughput in dryer

## Slide 5: Elements of process control system
CONTROLLER
SET POINT
INDICATOR
ACTUATOR
CONTROLLING ELEMENT
Measures controlled variable, transmits value to controller
Shows the measured value
Shows desired value of controlled variable
Compares measured value with set point, takes action to make them the same by sending a signal to actuator
Receives signal from controller to move controlling element
Adjusts manipulated variable to achieve control of controlled variable
SENSOR

## Slide 6: An example – water heating tank

## Slide 7: Lag and response time
The full effect of action by the controller does not immediately affect the controlled variable – there is a lag or delay in response.
Warmed water begins to be detected here
Temperature stabilises
Element on

## Slide 8: Overshoot and cycling about a set point
An on-off switch set to operate at a temperature T
When element is switched off, its residual heat continues to warm the water producing an overshoot
When element is switched on there is a lag before the element begins heating again.
T

## Slide 9: Types of automatic controller (1)
ON-OFF control
  the simplest and cheapest
  oscillates between fully on and fully off
  Not normally suitable for process control but OK for hot water heating, hot plates etc.
Proportional control (P)
  Control signal changes in proportion to difference between set point and measured value
  The closer the measured value to the set point the smaller the control signal – overshoot is minimised
Integral control (I)
  Controller takes action only if the set point and measured value remain different for a preset time
  Eliminates an ‘offset’ error inherent in P controllers

## Slide 10: Types of controllers (2)
Proportional control with reset (PI)
  This type combines both proportional and integral (or reset) actions
Derivative control (or Rate) D
  Controller action depends on the rate at which the controlled variable is changing
  This type of control anticipates the effect of large load changes and reduces the maximum error
PID control
  P provides basic control (with gain adjustment)
  I eliminates error between steady-state conditions and set point (with integral time adjustment)
  D reduces overshoot and noise (through derivative time adjustment)

## Slide 11: Control systems in the woolscour
Opening and computerised blending
  weighbelt systems
Level of wool in the feed hopper
  Photoelectric sensors
  Ultrasonic sensors
Scouring bowl temperature control
Flowback control
Flowdown of heavy liquors (FLOCOM)
Wool dryers
Supervisory control and data acquisition systems (SCOURCOM)

## Slide 12: Control of opening and blending
Multi-hopper weighbelt system used
Blend components loaded into feed hoppers
Each hopper drops contents onto common conveyor
Computer controls amounts of each component added

## Slide 13: Weighbelt feed control
Operates with feed hopper to maintain constant flow of wool
Load cell senses mass of wool on short conveyor
Controller receives signal to controller and belt speed from tachometer, calculates flow rate, compares with set point
Sends signal to motor to speed up or down accordingly
TACHOMETER
CONTROLLER
LOAD CELL
FEED HOPPER DRIVE MOTOR
FULCRUM
Conveyor rests on load cell
Conveyor pivots on fulcrum

## Slide 14: Controlling level of wool in hopper
HOPPERMATIC system uses hopper and weighbelt arrangement to control fee to scour
An ultrasonic sensor uses high-frequency waves to measure amount of wool in hopper and PID controller adjusts speed of motor on spiked lattice of first feed hopper
Other systems use photoelectric sensors
Source: Andar Holdings Ltd.

## Slide 15: Flowback control
Flowback controlled by float control valve or diaphragm
P control only is required
Some of the liquor from bowl 2 flows in just before the feed rollers of bowl 1

## Slide 16: Flowdown of heavy liquors
FLOCOM system measures relative density of liquor
Discharges heavy liquor from balance tank to maintain liquor density
Optical sensors may be used to monitor density
Solids may increase through increased wool flow or change in wool type

## Slide 17: Wool dryer control
Sensors can provide information on:
  Regain of wool leaving dryer
  Temperature inside dryer
  Humidity inside dryer
  Wool flowrate
Controllers can adjust:
  Heat supply to dryer
  Position of dryer exhaust damper
  Flow rate of wool to dryer
Even a well-controlled dryer needs even feed
Low regain variability into dryer ensures more uniformly dried wool leaving dryer

## Slide 18: Wool dryer control system
Moisture probes at end of dryer
Source: Streat Instruments

## Slide 19: DRYCOM 2000 System
Two PID controllers are used, with the control signal of one being the set point of the second
First controller uses regain value from moisture meter and outputs a control signal which is the temperature required to achieve the set point regain
Second PID loop uses temperature probe and adjusts heat input to give required temperature
ADVANTAGES: acts quickly, handles stoppages
Source: Streat Instruments

## Slide 20: Comprehensive control in scouring
SCOURCOM system (Streats) provides all functions of control and monitoring
Uses programmable logic controllers (PLC) to carry out control and data acquisition functions
Computer network reports current production and quality information communicated continuously to staff and management
Source: Streat Instruments

## Slide 21
End of Summary Slides
Close Window