## Slide 1: Conveying, Drying and Packaging of Scoured Wool
Topic 9
Notes: Mr Chairman
Members of the Board
Ladies and Gentlemen

## Slide 2: Methods of moving wool
Cart or forklift (small batches)
Single and double belt conveyors
Pneumatic systems

## Slide 3: Belt conveyors
Short brattices (or lattices) in machines
Long conveyors for moving wool two and from the scour train
For squeeze rollers steel wire mesh or plastic mats are suitable
Steel lattices are suitable for greasy wool
Double-belt conveyors are used for moving wool to a higher level
A ‘plough’ is used to deflect wool off a weigh belt

## Slide 4: Wire mesh mats
OPENER
SQUEEZE ROLLERS
Source: Taylor (1986)
Source: Taylor (1986)

## Slide 5: Pneumatic systems
Wool is blown or sucked through circular ducting
Scoured wool easier to move than greasy wool
Ducting may be metal or plastic
Inside must be smooth, with rounded corners
A fan creates air flow – placed at either of two positions
Blowing (fan before wool entry) – dust and fibres can find leaks and escape
Sucking (fan placed after wool leaves ducting) – no dust or fibre leaves system
Most systems allow entry or discharge of wool at different points

## Slide 6: Separating air and wool (1)
Perforated screen rotates and intersects the duct
Dust laden air (white arrow) passes through the screen and goes forward free of wool
SHIRLEY WHEEL
Source: Stewart (1988a)

## Slide 7: Separating air and wool (2)
Wool held on rotating perforated drum by suction
On reaching the baffle the wool falls off and through sealing rollers
The dusty air is drawn from the inside of the drum
ROTATING DRUM CONDENSER
Source: Stewart (1988a)

## Slide 8: Air and dust separation
A bag filter traps dust, but some fibres may work their way through to the outside
The operation of a cyclone gravity discharge resembles a whirlpool – the outer (downward) vortex forces the dust out the bottom; the inner (upward) vortex exhausts clean air to the atmosphere
Source: Stewart (1988a)

## Slide 9: Post-scouring dust removal system
Rotating Drum Condenser
Filter bags

## Slide 10: Wool drying
Regain: the weight of moisture in wool, expressed as a percentage of the dry weight
FORMULA:
  Regain(%) = 100 x weight of moisture / dry weight
Wool leaving final rinse bowl may have a regain of around 150%; needs to be dried to around 15%
Wool drying occurs through
  mechanical extraction by squeezing
  evaporation by heat in a dryer

## Slide 11: Wool dryers
Wool is held on perforated drums by air being sucked into drum
Screens over which wool passes have low porosity. Pressure drop across wool is small, giving even drying
Source: Amdar Holding Ltd.

## Slide 12: Considerations in wool drying
Moisture absorbing capacity of air increased by raising temperature
Rate of airflow is important (typically 3-4 metres per second used in dryers)
Moisture-laden air must be removed from dryer to admit fresh, dry air
Rate of feed must be constant to ensure consistent regain
Wool layer fed to dryer needs to have uniform thickness without gaps

## Slide 13: Other aspects of wool drying
A spiked brattice feed hopper between final squeeze press and dryer opens the fibres, gives constant feed and uniform thickness layer
A feed weighbelt, in conjunction with a double feed hopper, gives constant feed to the scour, with benefits in drying
Electronic control of dryer maintains required temperature –coupled to measurement of wool moisture as it leaves the dryer

## Slide 14: Pressing and Packing (1)
Once, greasy wool was shipped in bales of varying sizes and shapes – low densities (150-170 kg/m3) so costly to ship
Compressing bales into smaller volumes (dumping) gave increased densities (230-340 kg/m3) but no transport savings

## Slide 15
Dense dumping (compression of 2-3 bales) enables greasy wool to be packed to ~ 640 kg/m3; scoured wool – 510 kg/m3.
Dense baling: scoured wool compressed to 400-450 kg/m3 with presses of up to 600 tonnes thrust
Stowed in shipping container, holding 18-20 tonnes
Pressing and Packing (2)
Source: New Zealand Wool Services International Ltd.

## Slide 16
End of Summary Slides
Close Window