## Slide 1
Wool Requirements for Yarn Manufacture
Topic 2

## Slide 2: The number of thin places is determined by the average number of fibres in the cross-section
A yarn is an array of fibres held together by twist.
Notes: A yarn is an array of fibres held together by twist.
The properties of that yarn are basically determined by the properties of the fibres (diameter, length and strength), the uniformity of the number of fibres, and how well they are bound together by twist.

## Slide 3: The cross-section of a yarn will contain a greater number of fibres if the yarn consists of finer fibres. Thus, finer yarns are stronger, more even and have a better spinning performance but are more difficult to handle. Longer fibres give stronger yarns. Thus diameter and length are the key fibre properties for a yarn and its subsequent performance.

## Slide 4: Steps in Early Stage Wool Processing The main mechanical steps in worsted processing cover: Topmaking cleaning = scouring mixing = blending disentangling/individualising/cleaning = carding straightening = gilling (3 passages) removing entanglements, contaminants & short fibre = combing evening out = gilling (2 passages) Spinning thinning = drawing (3 to 5 gillings plus a roving passage) further thinning and first twisting = spinning removing faults = winding and clearing folding or plying = twisting

## Slide 5: Topmaking can be seen as the steps needed to present a clean, uniform product containing individualised, straightened fibres. Spinning is all the steps involved in turning top into a strong, continuous strand of twisted fibres ready for fabric manufacture. The fabric manufacturer will demand that the yarn match previous batches. It must be the same weight per unit length (count or tex), same colour and appearance and behave similarly. It must have adequate strength and abrasion resistance to survive weaving or low friction to run smoothly in knitting. It must be virtually free of faults and contamination.

## Slide 6: Is easily the most important fibre property It determines the average number of fibres in the yarn cross-section, and hence the yarn evenness, strength and spinning performance. It also determines the yarn and fabric bending stiffness and handle (for the same fabric construction and finishing).
Fibre Diameter

## Slide 7: Longer fibres enable fibres to wrap more securely and given stronger yarns and better spinning Stronger fibres give longer top but avoiding chemical damage is more important for yarn strength The spinner also requires the top be free from faults, contamination and short fibre to ensure smooth running at high speeds and to avoid rejection of the fabric

## Slide 8: The greasy wool specifications are designed to make sure that the diameter, length and cleanliness requirements of the top can be met. It is the art of the topmaker to produce the top for the lowest total price taking into account the cost of materials, production and losses. Spinning, which requires thinning and twisting of the fibre strand into a self-locking structure, is slow and much more expensive than topmaking and so the spinner’s requirements and needed fabric attributes drive the specifications.

## Slide 9
End of Summary Slides
Close Window