## Slide 1: Opening, Cleaning and Blending
Topic 8
Notes: Mr Chairman
Members of the Board
Ladies and Gentlemen

## Slide 2: Reasons for opening and cleaning
Blending combines diverse wool types to maintain quality and meet price level
Opening enables liquor to more easily penetrate all wools; cotted wools required special treatment
Dirt, dust etc. best removed when dry
Reducing amount of dirt entering scour liquor reduces effluent disposal costs
Scoured wools opened and cleaned to improve appearance

## Slide 3: The opening process
3 methods of opening: direct, interference, inherent
DOUBLE DRUM OPENER
Source: Taylor (1986)

## Slide 4: Self-cleaning screens
Retractable bar screens collect and remove dirt and fibre build-up from opener
Source: Andar Holdings Ltd. (a)

## Slide 5: Cyclic opener
Features: versatile, card-like action, intermittent operation, 1000-2000 kg/hr
Source: Taylor (1986)

## Slide 6: Decotter
For heavily matted or felted fleeces, fed separately
Some control over severity of opening
Processes about 250 kg/hr

## Slide 7: Feed hopper / opener combination
Two feed hoppers operating in tandem with a double drum opener
Includes feed control system
Performs opening and dirt removal before scour
Source: Andar Holdings Ltd. (a)

## Slide 8: Short Wool Processor
Separates and cleans short wools <100mm with maximum removal of VM, dirt etc.
Severity of action controlled by cycle time (3-15 sec)
Source: Andar Holdings Ltd. (b)

## Slide 9: Scoured Wool Cleaner
Based on WRONZ axial flow continuous dag crusher
Wools of all length processed; up to 2,500 kg/h
Source: Andar Holdings Ltd. (c)

## Slide 10: Automated blending before scouring
Source: Andar Holdings Ltd. (a)

## Slide 11: Step opener blender
Blending and dust removal after scouring
Source: Andar Holdings Ltd. (b)
Source: Stewart (1988)

## Slide 12: Batch blending system
Used for blending of carpet wools for woollen processing
Source: Houget Duesberg Bosson

## Slide 13
Bin blending system
Continuous system for fine wool scouring
Source: Andar Holdings Ltd. (a)

## Slide 14
End of Summary Slides
Close Window